## Slide 1
Considerations on R17 RRM enhancement scope
3GPP RAN #89e Sep. 14-18 2020 RP-201649 Agenda 9.1.2

## Slide 2
Considerations on R17 RRM enhancement scope
A few contributions regarding on Rel-17 RRM WI were sent to RAN #88e meeting
An email discussion which collects comments on these WI proposal is ongoing.
We provide our views on how to prioritize work items for Rel-17 in order to balance working loads and time limitation
In addition we provide our views on a few WI proposals.

## Slide 3
Considerations on R17 RRM enhancement scope
General considerations on RRM enhancement and MG enhancement
    17 new proposals on RRM enhancements(excluding CSI-RS) and 8 new proposals on MG enhancements(excluding NR-U and Positioning)
    How to prioritize new proposals for RRM enhancements and MG enhancements?
      Prioritize the proposals that is essential to the real deployments currently or in the near future.
      Limit the scope based on reasonable considerations about the workload and possible achievements in limited time scale and efficiency.
    How to treat leftovers from R16.
      For CSI-RS L3 RRM, the scope in R17 should be limited and it can be treated under R17 RRM enhancements.
      For Positioning, leftovers can be treated under R17 positioning WI.
      For NR-U, leftovers can be treated under R17 RRM enhancements if the proposals can be justified.

## Slide 4
Considerations on R17 RRM enhancement scope
Rel-17 RRM enhancements proposals that should be prioritized
  SRS antenna port switching
    Interruption is not specified even for EN-DC.
    NR CA/DC are also important scenarios.
  Active TCI-state switch for CSI reporting via CSI-RS reconfiguration
    Prefer to have some study on the possible delay requirements in NR.
    The issue is realistic and important.
  Inter-RAT NR measurement without gaps when configured with EN-DC
    For EN-DC configuration, gapless measurement is achievable when UE is configured with LTE SA and inter-RAT NR measurements.
    We see the benefit for particular deployment scenario
  HO with PSCell
    Important scenario for DC configurations.
    The scope of R17 discussion should be limited.

## Slide 5
Considerations on R17 RRM enhancement scope
Rel-17 RRM enhancements proposals that should be prioritized
  PUCCH Scell activation/deactivation
    Important scenario for FR2
  IDLE mode requirement for SMTC2-LP
    Discussion on requirements are needed, but whether to have additional requirements may depends on the outcome.
  TCI switching enhancement in REL-17
    Support. This can be considered if longer SMTC is configured.
    However, the priority of this can be further discussed based on operators input.
  UL gap and configuration for UE self-calibration and monitoring in FR2
    This is a realistic issue since R15.
    Spec impact is needed to better facilitate UE implementation.
    This is an issue resulted from UE RF but may need gap or scheduling restriction, which is in RRM scope. We are fine with either discuss in RRM or in RF.

## Slide 6
Considerations on R17 RRM enhancement scope
Rel-17 MG enhancements that should be prioritized
  Network Controlled Small Gap (NCSG) specification
    We understand the intention is to enable measurement during a period which otherwise will be wasted anyway.
    We think this one could have a relative high priority among all gaps related Wis.
  Multiple concurrent and independent MG patterns
    The proposal will benefit for multiple MOs scenario especially when the SMTC are not aligned. It will also bring more flexibility on network configuration. However the gap overhead should also be carefully studied.
  On-demand UE-initiated MG request
    It may beneficial for UE to improve the measurement efficiency for some particular deployment scenarios. Compared with other gap related Wis, its priority needs not be high.

## Slide 7
Considerations on R17 RRM enhancement scope
Rel-17 MG enhancements that should be prioritized
  Pre-configured MG pattern(s) per configured BWP (fast MG configuration)
    We see this WI will provide noticeable benefit either for fast MG configuration after BWP switch or increase flexibility of MG configuration.
  MG sharing enhancement
    Measurement gap sharing is only defined between intra-freq and inter-freq.
    Inter-RAT carriers can be prioritized in NR SA.
    The enhancements are needed.

## Slide 8
Considerations on R17 RRM enhancement scope
Summary our views on WIs for Rel-17 study
  WIs with the highest priority
    SRS antenna port switching
    Inter-RAT NR measurement without gaps when configured with EN-DC
    HO with PSCell
    PUCCH Scell activation/deactivation
    UL gap and configuration for UE self-calibration and monitoring in FR2 (Note: TBD in RRM_enh or FR2_enh)
  MG related WIs with the highest priority
    Multiple concurrent and independent MG patterns
    Pre-configured MG pattern(s) per configured BWP (fast MG configuration)
  Considering Rel-16 leftover issues, pragmatical thinking is encouraged to further limit the new introduced WIs for Rel-17 RRM,
    We suggest 5-6 items from Rel-17 RRM enhancement plus 3-4 additional gap related WIs are approved in the end.

## Slide 9
THANK
YOU