## Slide 1: Motivation for WID: Introduction of DL 1024QAM for NR FR1
Ericsson
3GPP TSG-RAN Meeting #89-e
Electronic Meeting, September 14-18, 2020
Agenda item: 9.1.2
RP-201673

## Slide 2: Motivation
Rel-15 NR supports downlink modulation order up to 256QAM for PDSCH.
LTE has introduced even higher order modulation order of 1024QAM for PDSCH in Rel-15.
NR should be competitive to LTE with regard to the spectral efficiency especially on refarmed operating bands and mid-bands, i.e., FR1
Even for NR, high SNR conditions supporting DL 1024QAM can be achievable in FR1 with:
  Small cell / indoor cell / non-sectorized cells
  Beamforming (in mid-bands 3-6 GHz)
It is expected that meeting EVM and demodulation requirements in the FR1 range should be similar to those for LTE from an implementation perspective and feasible.

## Slide 3: Summary of core WI objectives
Specify high order modulation for PDSCH [RAN1]
  Specify 1024QAM constellation as specified in E-UTRA for DL PDSCH
  Specify corresponding MCS table with 1024QAM entries as defined in E-UTRA
    Note: DCI overhead for MCS indication should be the same as in Rel-15
  Specify corresponding CQI feedback with 1024QAM entries as defined in E-UTRA
Specify corresponding RRC signalling and UE capabilities [RAN2]
  Note: DL PDSCH 1024QAM for FR1 should be defined as a per-band UE capability
Specify corresponding UE and BS RF core requirements [RAN4]

## Slide 4: Summary of performance WI objectives
Specify UE performance requirements for DL 1024QAM for PDSCH in FR1 and BS RF conformance tests in FR1 [RAN4]
  UE demodulation performance requirements for PDSCH.
  CQI reporting requirements.
  Conformance tests for BS RF.
  Note: UE demodulation and CQI requirements shall be defined for scenarios relevant for static links such as for fixed wireless access (FWA) links.