## Slide 1: Motivation EMC test simplification for MSR BS
Ericsson
3GPP TSG RAN Meeting #89e RP-201799
Electronic Meeting, September 14 - 18, 2020

## Slide 2: Background
Standards such as TS 37.113 define the BS test configurations that shall be used for demonstrating EMC conformance. These BS test configurations (TCs) are applied according to the declared RAT Capability Set (CS) of the Base Station (MSR) and the Band Category of the declared operating band (i.e. BC1, BC2 or BC3).
The TCs for MSR BS are defined in TS 37.141, and include 19 different capability sets (including 3 of single mode condition: WCDMA, LTE and NB-IoT standalone), which cover the possible RAT combinations available in a MSR BS.

## Slide 3: Justification
Current testing of EMC requirements as specified in standards such as TS 37.113 (MSR BS) considers many test configurations, due to various possible RAT combinations. Currently the Capability Sets for MSR standard add a new combination when a new RAT comes in. Even though, this principle looks for an understandable follow up of technical developments, it might not be the more efficient way from an EMC testing perspective. The increase in the number of combinations might lead to an increase in both the testing requirements and the testing cost (directly related to the testing time and resource).
Although EMC testing has some specificities that makes it different from RF testing, the TCs and CS used in EMC specs belong to the RF domain, which might lead to skip details that could contribute to simplify EMC testing. For example, EMC conducted emission and conducted immunity test methods and levels defined by IEC/CISPR are independent of the product (BS) characteristics and features, including the operating frequency or the Radio Access Technology (RAT).
CISPR 32 Annex B specifies the methods for exercising the EUT during EMC emission measurements. CISPR indicates that “For each function, or group of functions selected to exercise the EUT, a number of representative modes of operation, including low power/standby mode, shall be considered for testing. The mode(s) that produce(s) the highest emissions shall be selected for the final measurements.”
A simplification in the EMC testing could be achieved by considering the specificities of the EMC testing. An analysis of these characteristics might lead to alternatives such as the reduction in the number of RAT combinations defined in some Capability Sets, or the definition of Test Configurations and Capability Sets specifically devised for EMC tests. In both cases, the main goal would be a reduction in the costs associated to the EMC testing.

## Slide 4: Objective of Performance part WI
Specify how to handle the radiated emission limits for MSR (including AAS) within an EMC-only Capability Sets and Test Configuration.
  For BS equipment (ITU-R SM 329)
  For Ancillary equipment (CISPR 32)
Specify how to handle the radiated immunity limits for MSR (including AAS) within an EMC-only Capability Sets and Test Configuration.
Specify capability sets (only EMC) for MSR (including AAS):
  Emission testing
  Immunity testing
Specify test configurations (only EMC) for MSR (including AAS):
  Emission testing (except for the Radiated Spurious Part)
  Immunity testing
Evaluate the amount of reduction in test configurations achieved.
Define the required adjustments in the TS 37.113 chapter 4.5 according to the outcome of the previous steps.
Specify BS test configurations for EMC according to the results achieved in the WI.
Consolidate and Analyse the results obtained on EMC performance on different RATs for radiated and immunity testing.
Note: The starting point for the specification of capability sets and test configurations will be the existing ones defined in TS 37.141.