## Slide 1: Coverage Enhancement study and WI scope for Rel-17
9.7.4
3GPP TSG RAN Meeting #90-e RP-202302
Electronic Meeting, December 7 - 11, 2020

## Slide 2: Coverage Enhancement study results
NR coverage evaluation for baseline case of both FR1 and FR2 has lead to conclusion of potential coverage bottleneck For FR1 :
1st priority
  PUSCH for eMBB (for FDD and TDD with DDDSU, DDDSUDDSUU and DDDDDDDSUU)
  PUSCH for VoIP (for FDD and TDD with DDDSU, DDDSUDDSUU)
2nd priority
  PRACH format B4
  PUSCH of Msg.3
  PUCCH format 1
  PUCCH format 3 with 11bit
  PUCCH format 3 with 22bit
  Broadcast PDCCH
For FR2 :
  PUSCH eMBB (DDDSU and DDSU)
  PUSCH VoIP (DDDSU and DDSU)
  PUCCH F3 11bits
  PUCCH F3 22bits
  PRACH B4
  PUSCH of Msg3

## Slide 3: Over all progress of Coverage Enhancement
Significant work was done in the study phase by common evaluation methodology and assumption
WI scope of candidate solutions to be considered:
  PUSCH: Repetition Type A Enhancement, DMRS bundling, TB over multiple-slot are recommended in the TR
  PUCCH: DMRS-less, Type B repetition, Dynamic repetition and DMRS bundling across PUCCH repetitions are discussed
  Other chancels: RACH, Msg3, Msg4, Broadcast PDCCH, PUCCH for Msg4, SSB and beam reporting enhancement are discussed
On the next step work for Coverage Enhancement
  Sufficient study has been done and we can conclude several channels need to be enhanced
    Work Item should be started for enhancement at least following channels: PUSCH, PUCCH
  Tasking the specification of the enhancement solutions among the study list into the WI
  Further identifying the coverage target for the enhanced channel base one the evaluation results
    The detailed target can be either made with decision in RAN or following WI

## Slide 4: WI scope of PUSCH
  The PUSCH has the lowest coverage performance in most of the scenarios
  The technical report already recommend 3 schemes for coverage enhancement
  The Repetition Type A is slot-based and the TB over multiple slot would results in similar specification
  Considering merge the 2 schemes into one category for normative work
  A common set of solution can be targeted
  Specify the definition of the available slots/symbols and the TBS determination schemes DMRS bundling over multiple-slot could be supported
  Specification change will be conducted in DMRS configuration, hopping scheme and phase continuity requirement to enable the multiple-slot channel estimation.
  Study has conclude basic PUSCH enhancements, further discuss and justify
  Power boosting for pi/2 BPSK for PUSCH for PC2 UEs
  Sub-PRB transmission with multi-slot aggregation

## Slide 5: WI scope of PUCCH
Motivation for PUCCH coverage enhancement
  PUCCH has similar coverage gap as for PUSCH in most of scenarios
  If PUSCH is enhanced, it would be likely outperforming PUCCH without enhancement
  PUCCH is “harder” coverage limit than PUSCH, which would be more flexible in terms of coverage by link adaptation as a data channel
WI should at least include several PUCCH enhancements
  The DMRS-less PUCCH format can achieve better gain on top of existing repetition and hopping schemes
    The RF requirement for the new format should be introduced
  Dynamic repetition scheme can be supported with minimize specification effort
  DMRS bundling across PUCCH repetitions should be supported as same phase continuity requirement as for PUSCH
  RAN1 can study whether to reuse Type B PUSCH hopping into PUCCH coverage enhancement

## Slide 6: WI scope of other channels
Targeting on small number of enhancements
  RACH and Msg3 can be enhanced
    The channels show gaps in certain scenarios and they are key channels for the overall coverages
  The remaining Msg4, Broadcast PDCCH, PUCCH for Msg4, SSB and beam reporting enhancement can be selected
    Significant justification should be required for the remaining channels

## Slide 7: Coverage enhancement related to other WIs
  RAN1 should avoid duplicated specification efforts into same issue
  Working scope distinction for Coverage Recovery of RedCap and Coverage Enhancement by:
    Different Channels to be enhanced
      For PUSCH and Msg3 PUSCH, the enhancement should be mainly in CE WI due to significant amount of coverage gaps and candidate solutions in CE SI
      RedCap WI can include coverage recovery of PDCCH CSS, Msg2 and Msg4(If they are concluded), which are mainly DL channel
    Different coverage targets from different SIs, if identified, can further categorize the candidate solutions
      It may lead to different WIs

## Slide 8
THANKS