## Slide 1: Motivation for the Study on Dynamic OTA Testing for FR2
3GPP TSG RAN Meeting #90e
Electronic Meeting, Dec. 7 - 11, 2020
RP-202632

## Slide 2: Discussion on Dynamic-geometry based FR2 OTA Test in Rel-15 and -16
Discussion contributions and WFs about Dynamic-geometry based FR2 OTA
  3GPP TSG-RAN WG4 NR ad hoc #3, Nagoya, Japan, 18 – 21 Sep 2017
    R4-1709867, WF on channel modelling, Keysight Technologies, Rohde & Schwarz, Anritsu, Spirent, Intel, Qualcomm
    R4-1710028, WF on RRM baseline setup, Rohde & Schwarz, Intel
    R4-1709862, Request for input on key deployment factors for definition of link-level channel models for RRM and demod requirements, Keysight Technologies
    R4-1709837, Test scenarios and test system complexity for RRM OTA testing, Rohde & Schwarz
  3GPP TSG RAN WG4 Meeting #84bis, Dubrovnik, Croatia, 9 – 13 October 2017
    R4-1711308, On the dynamic channel model, Huawei, HiSilicon
  3GPP TSG-RAN4 Meeting #85, Reno, Nevada, USA, 27 November - 1 December 2017
    R4-1713050, UE Test Coverage in mmWave NR, Anritsu, Azimuth Systems
    R4-1712702, Spatial impact on demodulation requirements, Keysight Technologies
    R4-1712695, Test scope for NR initial access and beam management at FR2, Keysight Technologies
  3GPP TSG-RAN WG4 Meeting #86, Athens, Greece, 26 Feb - 02 Mar 2018
    R4-1712695, Test scope for NR initial access and beam management at FR2, Keysight Technologies
  And there have been more papers
Discussion contributions and WFs about Dynamic-geometry based OTA in Rel-15

## Slide 3: Discussion on Dynamic-geometry based FR2 OTA Test in Rel-15 and -16
Rel-16 Study Item on “Radiated metrics and test methodology for the verification of multi-antenna reception performance of NR UEs [FS_NR_MIMO_OTA_test]” includes the following objectives as the second priority (RP-192416)
  MIMO throughput in a dynamic geometry environment is the second priority
  Extension of Rel-15 RRM tests to include dynamic geometry
As per the SID, RAN4 discussed “UE-orientation rotation only based semi-dynamic geometry based FR2 performance tests methodology”, however, due to lack of time, RAN4 couldn’t reach a conclusion in the last meeting of the SI RAN4#95-e and captured a unanimous view on this in R4-2008865 as below
  FR2 Dynamic testing (Beam Switching/Refinement testing)
    NO conclusion in Rel-16 MIMO OTA test SI.
    Views on this topic is collected:
      Option 1: YES
      Option 2: No requirements (Huawei)
      Option 3: Further study in the Rel-17 WI (Sprient, keysight, Qualcomm)
      Option 4: Further study dynamic test in a separate SI in future release (keysight, Huawei, Samsung, Oppo, Sprient, CAICT, Qualcomm)
Discussion and conclusion for Rel-16 MIMO OTA SI

## Slide 4: Discussion on Dynamic-geometry based FR2 OTA Test in Rel-15 and -16
In Rel-15 and -16, RAN4 established a common understanding that Dynamic-geometry FR2 OTA Testing should be further studied.
Necessity of Dynamic-geometry FR2 OTA Testing was presented/discussed by many companies in Rel-15 NR.
Details of Dynamic-geometry FR2 OTA Test mechanism scope was extensively discussed in Rel-16 MIMO-OTA Study Item.
Summary of 3GPP discussion on Dynamic-geometry based FR2 OTA Test

## Slide 5: Motivation of Dynamic-geometry based FR2 OTA Test
The key enablers of high throughput for FR2 are analog/hybrid beamforming techniques which should be rigorously verified by corresponding tests. However, the current test mechanisms defined in 3GPP have the following restrictions:
  Once UE orientation and test direction are determined before a test, these remain the same during the test
  Even in cases where performance is measured over multiple test directions, enough beam-dwell time in-between test geometry updates is given for the UE such that Dynamic Beam Management is NOT really tested
  The above restrictions make FR2 test results too optimistic, and hence, these do NOT reflect the real user experience.
Besides, considering FR2 UE beam management consumes nonmarginal power and time, there can be UEs reducing beam management frequency and/or a search space size of UE beam codebook to the point where throughput and mobility performances are degraded. However, the performance impacts due to the improper Beam Management are NOT accounted for in the current 3GPP FR2 test methodologies.
Problem statement

## Slide 6: Test Coverage and Restriction of Current FR2 OTA
Mobility/Demodulation Performances under Ideal/Deterministic Beam Condition
CSI-RS based narrow beams
SSB based broad beam
Handover b/w Cells
Serving gNB’s narrow beam switch
Serving gNB’s
wide beam switch
MIMO sensitivity
performance
time
SNR 5dB
SNR 5dB
Effectively off
Effectively off
0.6sec
30 SSBs
0.4sec
20 SSBs
0.4sec
20 SSBs
time
3sec
Beam initialization
Performance
measurement
Mobility related tests
(no-concurrent active Tx beam)
MIMO sensitivity tests
(Beam Selection Time)
3sec
Performance
measurement

## Slide 7: Test Coverage and Restriction of Current FR2 OTA
UE performance in terms of Beam Management is not included in Performance Assessment procedure
Chamber Tx
RSRP
(SNR and BLER will follow a similar tendency)
time for beam-refinement
temporary disconnection
(recovery procedure can be detected)
Covered by the current test procedure/requirements
(mean RSRP differs between test directions mainly due to UE directivity gain imbalance over sphere)
Currently excluded from valid data set for performance assessments
(RSRP drop, PDCCH missing, Link recovery procedure, etc.)

## Slide 8: Examples of Operator specific Field Requirements focusing on BM
    Graphical analysis (record and plot the following on a geographic map of the drive route)
  gNB serving beam index
  SS-RSRP and SS-SINR
  PDSCH/PUSCH throughput
  Beam failure and recovery events
    Statistical analysis
  gNB serving beam dwelling time
  UE Rx beam dwelling time
  Number of beam switches
  Number of beam failure events
  Beam recovery success rate
  Beam recovery latency
  Note that the above observation may not be consistent over time, e.g. differ depending on gNB scheduler, gNB beam allocation, scattering environment, etc.
Field Certificate/Compliance Tests

## Slide 9: Benefits of Dynamic-geometry based FR2 OTA Test
With a standardized FR2 Dynamic-geometry based OTA test system, the following performance evaluation approaches can be effectively reduced for integrated UE performance assessments
    Field test-based integrated UE performance assessment
    Proprietary Lab solutions-based UE performance assessment
  Note that both above approaches are time and cost prohibitive. In addition, there will be significant uncertainties that make performance analysis and optimization difficult.
Benefits
 | Cost | Repeatability | Comment
Field test-based approach | ↑ | ↓ | for analysis, hard to decouple multiple contributors
Proprietary-based approach | ↑ | ↓ (between TEs) | may have reliability issues
3GPP standardized approach | ↓ | ↑ | can be easily repurposed for field issue reproduction/R&D/etc

## Slide 10: Benefits of Dynamic-geometry based FR2 OTA Test
Benefits
3GPP conformance test methodologies
Additional Lab Certification Tests
Static-geometry
Hard to debug issues and optimize/analyze performances due to low repeatability
Conventional Static-geometry approach
Proposed Dynamic-geometry approach
Field Certification Tests
Operator specific tests
Additional Lab Certification Tests
Static-geometry
Field Certification Tests
Dynamic-geometry
Issued found in Field Test can be reproduced in the Lab to some extent by Dynamic-geometry test setup
Test coverage can be reduced
Field Test Coverage can be effectively reduced

## Slide 11: Proposal for Dynamic-geometry based FR2 OTA Test
Dynamic-geometry based FR2 OTA Testing Platform/Procedure
  The main objective is to establish new test platform/procedures rather than introducing new requirements under dynamic-geometry environment
Phase-I (UE autonomous BM in a Single-cell)
  Serving gNB DL beam doesn’t change but UE Tx/Rx beam needs to be updated to maintain link and continue transmitting and receiving UL/DL signals.
  Note: Based on Rel-16 MIMO-OTA SI outcome (reusing 3D-MPAC system)
Phase-II (UE BM based on interaction with Multi-cells)
  UE travels across cell boundary and receives both desired and undesired signals from multiple cells.
  Note: RAN4 will not start Phase-II before Phase-I completion.
Main goal and scenarios