## Slide 1: Applications of Artificial Intelligence in MIMO Networks
3GPP TSG RAN Meeting #90e
Electronic Meeting, December 7-11, 2020
Source: ZTE, Sanechips
Agenda: 9.12
RP-202674

## Slide 2: Introduction
  New SID: Study on further enhancements for data collection (RP-201304) has been approved in RAN#88e. The major objective is:
  Study high level principles for RAN intelligence enabled by AI, the functional framework (e.g. the AI functionality and the input/output of the component for AI enabled optimization) and identify the benefits of AI enabled NG-RAN through possible use cases e.g. energy saving, load balancing, mobility management, coverage optimization, etc.
  It was discussed whether "beam management" is explicitly listed as one of the possible use cases. However, it was removed due to the possible need of RAN1 involvement. Nevertheless, companies have shown their strong interest in AI applications on physical layer. We see the need of studying standardization impact of AI applications in both higher layer and physical layer aspects.
  In this contribution, we discuss the potential AI applications in MIMO networks.

## Slide 3: Potential Benefits
    AI algorithms are used in the current networks
      However, limited applications in PHY due to complexity and lack of coordination between gNB and UE
    Enhancements (e.g. by providing assisted information) can be beneficial to achieve faster/more accurate learning.
    gNB and UE can collaborate on training and execution to reduce complexity.
    Machine learning for MIMO has been drawn a lot of interest in recent research.
    The potential benefits are:
      Acquiring more accurate channel information with less CSI feedback overhead
      RS overhead can be reduced for CSI acquisition/beam management or demodulation
      Reduce control signalling overhead
    These potential benefits translate to better system performance e.g. in terms of throughput and reliability

## Slide 4: Generic model of AI and its standardization impacts
Feedback from UE helps AI training for better prediction at gNB
AI outcome from gNB is signaled to UE for better operation
UE execute based on training result from gNB and local input
AI black box located at gNB or UE
either from UE or gNB itself
Feedback from UE based on output of AI prediction at UE
Potential standardization impacts:

## Slide 5: AI for Mobility and Beam Management
AI model: Action for now(t0) or prediction for future(t1,t2...) for one UE is deduced based on measurement/event from related UEs jointly by taking their history(t-1,t-2...) and position stamp (p+m) into account. e.g. scheduling/beam tracking at gNB
UE may predict future event/measurement (t1) by running AI algorithm based on measurements in the past (t-1,t-2). Predicted result is fed back to gNB e.g. mobility/beam prediction at UE
AI
UE1(Meas(t+n,p+m), n<=1,m>=0)
UE1[Action(t+n,n>=0)]
UE2(Meas(t+n,p+m), n<=1,m>=0)
UEk(Meas(t+n,p+m), n<=1,m>=0)
UE2[Action(t+n,n>=0)]
UEk[Action(t+n,n>=0)]

## Slide 6: Predictable Mobility for Beam Management
Beam dwelling time depends on multiple factors including UE speed, distance between gNB and UE and beam-width of the beams.
It can be observed that the beam dwelling time can be as small as 7ms. With the current beam management procedure including beam reporting, beam group activation and beam indication, it is hard to meet this beam update requirement. To make sure narrow beams can be used for better coverage and performance in high speed scenarios, it is beneficial to use AI on beam prediction together with trajectory prediction for mobility.
Potential standardization impacts include enhancements on beam reporting, beam activation and beam indication.
Effective coverage depending on beam-width, distance and speed

## Slide 7: Predictable Mobility for Beam Management
When mobility is predictable, beam management can be also predictable.
With predictable beam management based approach, it can be observed that significant performance gain is obtained due to RS overhead reduction and/or narrow beams.
Details can be found in RP-202675.
HST trajectory with RRHs

## Slide 8: CSI prediction in frequency domain for CSI acquisition
FDD channel reciprocity with limited CSI feedback
  FDD channels also have reciprocity in the sense of UL and DL essential paths which are often sparse
  By machine learning, FDD DL channel can be obtained via channel reciprocity with limited feedback
Potential enhancement: Parameterized CSI feedback for limited subcarriers
Fig 1. CDF curves of correlation between estimated and real DL channel response

## Slide 9: CSI compression feedback based on AI: general procedure
AI algorithm can compress the channel coefficient vectors in both spatial and frequency domain to a new coefficient vector with smaller size, to optimize the system performance v.s. overhead.
  More accurate CSI feedback can enable better MU operation for massive MIMO
For a trained AI algorithm in UE or BS side
  At UE: Input is the original channel coefficients measured from P CSI-RS ports in M RBs, and output is a new coefficient vector with smaller size. The size of the new coefficient vector depends on compression ratio, which is the ratio between the overhead to report the original channel matrix and the overhead to report the compressed coefficients.
  At BS: Input is the compressed coefficient vector received from UE, and output is the recovered channel coefficients for all the M RBs.

## Slide 10: CSI compression feedback based on AI: evaluation results
Evaluations are conducted to show the benefit of AI based approach to compress and feed back CSI.
BS has 32 antennas. UE has one receive antenna. The bandwidth has 125 RBs.
Baseline is the Rel-16 eType II codebook to compress channel matrix in spatial and frequency domain.
X axis is the compression ratio. Y axis is Generalized Cosine Similarity (GCS) between two channel vectors and defined as .
It can be observed for a given compression ratio, AI based approach shows significant gain over Rel-16 eType II in terms of GCS, which reveals the GREAT potential of AI based approach.

## Slide 11: CSI prediction in time domain for demodulation
Potential enhancement: Support more flexible DMRS indication, RS overhead reduction

## Slide 12: Potential enhancements for AI applications in PHY aspects
Potential enhancements for Beam Management
  Beam tracking for predictable mobility
  Enhancements on beam reporting, beam activation and beam indication
  Beam selection based on varying traffic type and UE distribution
Enhancements for AI on CSI feedback/prediction
  CSI/interference prediction in time/frequency domain
  Parameterized/compressed CSI feedback
  Reduction on RS overhead and measurement
  Adaptive antenna/beam group selection
  Downloadable codebook

## Slide 13: Potential enhancements for AI applications in PHY aspects
Potential enhancements for AI on channel prediction for demodulation
  RS overhead reduction by sharing DMRS across frequency/time domain or by using SRS for demodulation
  Required signalling to assist or align the channel prediction between gNB and UE
Potential enhancements for AI on MCS selection
  Feed back channel/interference information to assist outer loop link adaptation for MCS selection
  UL MCS selection by UE
Potential enhancements for AI on resource allocation
  Multi-slot resource allocation
  Proposal: Consider the above potential enhancements for standardization on AI.

## Slide 14: Thanks