## Slide 1: Motivation of sidelink over unlicensed spectrum
3GPP TSG RAN Meeting #91-e RP-210255
Electronic Meeting, March 22 - 26, 2021

## Slide 2: SL and Uu
Advantage of SL
  Latency reduction
    Direct instead of indirect communication
  Traffic offloading
    Traffic over Uu interface is saved for sidelink
  Higher spectrum efficiency
    Only one instead of two sets of radio resource
  Coverage extension
    UE can connect to network via relay (U2N) or
    UE can connect with each other out of coverage (U2U)
Collaboration between SL and Uu
  Smooth mobility and service continuity
    Service can continue with normal indirect communication when a pair of UEs can’t reach with each other directly and vice versa
  Coordination
    For some use cases e.g. CV2X, IIoT, NCIS, Uu link and sidelink communication are organic part of one system i.e. they collaborating with each other

## Slide 3: Unlicensed spectrum
Notes: Huanglei: any impact to SL-U due to different regulation on transmission power e.g. indoor case
The EU part should be updated to 5.945GHz ~ 6.425GHz

## Slide 4: Motivation of SL-U
Co-existence on unlicensed spectrum
  Simulation shows SL-U can co-exist with other technology e.g. wifi
SL-U can provide for CV2X and NCIS with e.g. high throughput
  Which can’t be met by current sidelink communication based on limited licensed spectrum
SL-U can meet some of the requirements of e.g. IIoT
  i.e. requirements can be met by both licensed and unlicensed spectrum
SL-U can also used in other commercial use cases which may or may not require Uu link collaboration e.g. smart home
  Those function can be from the same platform as NCIS e.g. a smart phone
Vertical e.g. V2X, IIoT, etc.
Smart home
Commercial e.g. NCIS, wearable device etc.

## Slide 5: NCIS use cases
XR gaming
  Co-located users exchange live streams and control signal with each other and/or centralized game service
Real-time sharing of XR content
  A bidirectional or unidirectional A/V channel could be open between users to exchange real-time stream of motion signals and effects that influence the rendering of the 3D object
Media sharing
  Offline sharing is used for sharing 3D models/objects and 3D MR scenes amongst UEs
Wireless tethered connection
  AR/VR glass or helmet-mounted etc. could be tethered to a smart phone
[1] TR 26.928 Extended Reality (XR) in 5G

## Slide 6: NCIS Requirement(s)
[1] 22.261 table 7.6.1-1 KPI Table for additional high data rate and low latency service
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity |  | 
 | Max Allowed End-to-end latency | Service bit rate: user-experienced data rate | Reliability | # of UEs | UE Speed | Service Area (note 2)
Gaming or Interactive Data Exchanging (note 3) | 10ms (note 4) | 0.1-[1] Gbit/s supporting visual content (e.g. VR based or high definition video) with 4K, 8K resolution and up to120fps content. | 99.99% (note 4) | ≤ [10] | Stationary or Pedestrian | 20 m x 10 m; in one vehicle (up to 120 km/h) and in one train (up to 500 km/h)
Consume VR content via tethered VR headset (note 6) | [5 -10] ms (note 5) | 0.1-[10] Gbit/s (note 5) | [99,99%] | - | Stationary or Pedestrian | -
NOTE 2:Length x width (x height). NOTE 3:Communication includes direct wireless links (UE to UE). NOTE 4: Latency and reliability KPIs can vary based on specific use case/architecture, e.g. for cloud/edge/split rendering, and may be represented by a range of values. NOTE 5: The decoding capability in the VR headset and the encoding/decoding complexity/time of the stream will set the required bit rate and latency over the direct wireless link between the tethered VR headset and its connected UE, bit rate from 100 Mbit/s to [10] Gbit/s and latency from 5 ms to 10 ms. NOTE 6: The performance requirement is valid for the direct wireless link between the tethered VR headset and its connected UE. |  |  |  |  |  | 

## Slide 7: IIOT use case(1/2)
[MPR-22832-6.6-00a] The 5G system shall allow UEs to use ProSe communication when the UEs are not served by a RAN.
[MPR-22832-6.6-00b] The 5G system shall be able to support ProSe communication between UEs in close proximity using spectrum different than the spectrum being used for the 5GC-based communication.
[MPR-22832-6.6-00c] The 5G system shall be able to support 5G LAN-type service to UEs using ProSe communication.
[MPR-22832-6.6-00d] The 5G system shall be able to support multicast communication between the UEs within the group of UEs connected by ProSe communication.
[MPR-22832-6.6-00f] The 5G system shall be able to support mobility of the group of UEs connected by ProSe communication with respective service performance requirements in Table 6.4-1.
[MPR-22832-6.6-00i] The 5G system shall be able to support service continuity of a group of UEs using ProSe communication with respective service performance requirements in Table 6.4-1 when the group moves between a non-public network and a PLMN (subject to operator policies and agreement between the operators and service providers).
[1] 22.832 v17.20 Study on enhancements for cyber-physical control applications in vertical domains

## Slide 8: IIOT use case(2/2)
Use case | Characteristic parameter |  |  |  |  |  | Influence quantity |  |  |  | 
5.11 – Cooperative carrying of work pieces | Communication service availability: target value in % | Communication service reliability: Mean Time Between Failure | End-to-end latency: maximum | Bit rate | Direction | Message Size [byte] | Transfer interval [ms] (note 2) | Survival time [ms] (note 2) | UE speed [km/h] | # of UEs connection | Service Area [m³] (note 1)
Cooperative carrying – fragile work pieces | 99,9999 % to 99,999999 % | ~ 10 years | < 0.5 * Transfer interval | 2.5 Mbit/s | UE-UE (ProSe communication) | 250 500 with localisation information | > 5 >2.5 >1.7 | 0 Transfer interval 2 * Transfer interval | ≤6 | 2-8 | 10 x 10 x 5; 50 x 5 x 5
Cooperative carrying – elastic work pieces | 99,9999 % to 99,999999 % | ~ 10 years | < 0.5 * Transfer interval | 2.5 Mbit/s | UE-UE (ProSe communication) | 250 500 with localisation information | > 5 >2.5 >1.7 | 0 Transfer interval 2 * Transfer interval | ≤12 | 2-8 | 10 x 10 x 5; 50 x 5 x 5
NOTE 1: Service Area for direct communication. The group of UEs with direct communication might move throughout the whole factory site (up to several km²) NOTE 2: The first value is the application requirement, the other values are the requirement with multiple transmission of the same information (two or tree times respectively). |  |  |  |  |  |  |  |  |  |  | 
[1] 22.832 v17.20 Study on enhancements for cyber-physical control applications in vertical domains
Table 5.11.6-1: KPIs for ProSe communication for cyber-physical control applications

## Slide 9: CV2X use case
High degree or fully automation requires:
  Exchange of raw or processed data gathered through local sensors
  Live video images among vehicles, road site units, devices’ of pedestrian and V2X application servers
22.186 Enhancement of 3GPP support for V2X scenarios; stage 1
Communication scenario description |  | Req # | Payload (Bytes) | Tx rate (Message /Sec) | Max end-to-end latency (ms) | Reliability (%) | Data rate (Mbps) | Min required communication range (meters)
Scenario | Degree |  |  |  |  |  |  | 
Sensor information sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-001] | 1600 | 10 | 100 | 99 |  | 1000
 | Higher degree of automation | [R.5.4-002] |  |  | 10 | 95 | 25 (NOTE 1) | 
 |  | [R.5.4-003] |  |  | 3 | 99.999 | 50 | 200
 |  | [R.5.4-004] |  |  | 10 | 99.99 | 25 | 500
 |  | [R.5.4-005] |  |  | 50 | 99 | 10 | 1000
 |  | [R.5.4-006] (NOTE 2) |  |  | 10 | 99.99 | 1000 | 50
Video sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-007] |  |  | 50 | 90 | 10 | 100
 | Higher degree of automation | [R.5.4-008] |  |  | 10 | 99.99 | 700 | 200
 |  | [R.5.4-009] |  |  | 10 | 99.99 | 90 | 400
NOTE 1: This is peak data rate. NOTE 2: This is for imminent collision scenario. |  |  |  |  |  |  |  | 
Table 5.4-1 Performance requirements for extended sensors

## Slide 10: Smart home
Use case:
  Electronics at home could be connected with each other or controlled by smart devices
Requirements
  Data rate could be up to 500Mbps
  Latency could be low to 10ms
  Connectivity could be around 50+

## Slide 11: Co-existence simulation result
Solid line: wifi only
Dashed line: 50% UE is replaced with SL-U UE
Observation: throughput of Wifi UEs is actually improved after same amount of Wifi UE is replaced with SL-U UE

## Slide 12: Deployment scenarios
Scenarios:
  Support in-coverage, partial coverage and out of coverage scenarios
Resource allocation：
  At least support mode 1 and mode 2 or new resource allocation scheme introduced in R17
Single carrier or multiple carriers
  Aggregation between unlicensed and licensed carrier is also supported

## Slide 13: Main building blocks for SL-U
SL-U
Multi carrier operation based on LTE-CV2X
FR2 features and WI on 60GHz
Rel17 SL enhancement
URLLC/IIOT on unlicensed spectrum
Features of NR-U including LBT and LBE operation
WI on Redcap UE

## Slide 14: Objectives
Covering frequency bands in 5GHz, 6GHz and 60GHz
In coverage, partial coverage and out of coverage scenarios are covered.
No inter RAT control scenario is considered and only NR SA architecture should be used in this item
Requirement for advanced V2X services, commercial uses e.g., NCIS and XR service should be taken into account for sidelink in this item
  Unlicensed channel access scheme and coexistence with other technology e.g., Wi-Fi (RAN1)
  Specify any changes in resource allocation scheme (e.g., Mode 1 and Mode 2)
  Specify any changes in existing sidelink slot structure as necessary (e.g., due to LBT, new numerologies, etc) (RAN1)
  Specify any changes in sidelink channels and signals (e.g., due to OCB requirement, high frequency operation, etc) (RAN1)
  Specify any changes in physical layer procedures necessary to operate sidelink in unlicensed spectrum (e.g., HARQ procedure, power control, beam management, time line related procedures, etc.) (RAN1, RAN2)
  Specify multiple carrier operation (RAN1, RAN2)
  7. Specify related L2 procedure and control plane procedure (RAN2)
  8. Specify necessary RF requirements for transmitting sidelink signals and channels in unlicensed spectrum of 5GHz, 6GHz and 60GHz (RAN4)