## Slide 1: Motivation of study on radio enhancement based on AI
3GPP TSG RAN Meeting #91-e RP-210256
Electronic Meeting, March 22 - 26, 2021

## Slide 2: OPPO’s vision in decades
eMBB
eMBB,IoT,XR
AI by 5G
XR,AI
2010
4G
2020
5G
2025
5G Pro
(AI for 5G)
2030
6G
AI of 5G

## Slide 3: AI or ML or DL
AI
ML
DL
Multilayer neural network
Handle complex but specific use cases e.g. AlphaGo
Assorted learning techniques
Augmented intelligence e.g. search engine
Computer and algorithm such ML and DL
Mimic human intelligence e.g. Skynet

## Slide 4: AI/ML categories
AI/ML
Structured Source data
Known model
Rule or transfer function
Supervised learning
Reward
Feedback data
Converged rule or transfer function
Reinforcement learning
Action
unstructured Source data
Rule or transfer function
unsupervised learning
server
Source data
Source data
Source data
server
server
server
server
model
weight
model
weight
model
weight
Federated
Distributed
Centralized
Offline
Offline
Online

## Slide 5: AI by 5G
Key issues are studied in SA1(AMMT SID):
  Data exchange upon training or inference between server and endpoints for e.g. image/voice recognition etc
  AI/ML model distribution or management as a service
The AI traffics are different
  In terms of QoS requirement e.g. experienced data throughput, latency etc.
New solution is needed to address these new AI traffics
Use case analysis is done and performance KPI will be defined at next SA1 meeting
TR 22.874

## Slide 6: Principles and framework @ FS_NR_ENDC_data_collect
The following high level principles should be applied for AI-enabled RAN intelligence:
  The detailed AI/ML algorithms and models for use cases are out of RAN3 scope.
  The study focuses on AI/ML functionality and corresponding types of inputs/outputs.
  The input/output and the location of AI inference should be studied case by case.
  Training aspects are FFS
  NG-RAN is prioritized; EN-DC is included in the scope. FFS on whether MR-DC should be down-prioritized.
  A general framework and workflow for AI/ML optimization should be defined and captured in the TR. The generalized workflow should not prevent to “think beyond” the workflow if the use case requires so.
[1] 37.817 Study on enhancement for Data Collection for NR and EN-DC

## Slide 7: Typical use case in wireless communication system
Non-real time use case:
  System level:
    NWDAF to maintain the network by operator
  Cell level:
    QoE optimization
    Network energy saving
    Network load balancing
    Mobility optimization
    Coverage optimization
    Traffic steering
    …
Real time use case(link level):
  UE specific
    CSI compression
    MIMO beam forming and selection
    Channel estimation and modelling
    Link adaption e.g. MCS
    Receiver enhancement
    …

## Slide 8: ML algorithm applicability
CN
OAM
CU
DU
ML algorithm complexity
ML algorithm Real time, power consumption requirement
Non-real time use cases
Real time use cases

## Slide 9: Two basic ML approaches
ML approach is applied for one specific step in the processing chain
ML approach is applied for contiguous multiple steps or whole processing chain
Or mixed of two approaches
MAC
Coding
Modulation
…
Antenna mapping
MAC
ML based Coding
Modulation
…
Antenna mapping
MAC
ML based coding, modulation…
Antenna mapping
MAC
Coding
Modulation
…
Antenna mapping

## Slide 10: Standard impact
For case 1 and case2:
  No standard impact at all i.e. purely implementation
Case3: AI/ML algorithm may need some new input and/or output to/from other nodes
Case4: Same AI/ML algorithm to accomplish same task in distributed way but the output/input in-between could be a container. Input and output of algorithm should be standardized
Case5: Different AI/ML algorithm accomplish same task in distributed way. Output and Input over interface may need standardization
Case1
Case2
Case3
Case4
Case5

## Slide 11: CSI compression
The basic idea:
  The measured raw CSI is compressed by a DML algorithm
The benefit:
  More precise channel status information can be transferred in order to improve MIMO performance
AI based CSI vs 3GPP CSI code book
Measured raw CSI
DML F(x)
Compressed CSI
Measured raw CSI
DML F-1(x)
Compressed CSI

## Slide 12: Receiver with noise-compression
Basic idea:
  DnCNN helps to remove some noise for pilot and data
Benefit: to improve the SNR and BER
Simulation assumption | value
Number of Tx antenna | 2
Number of Rx antenna | 2
Subcarriers | 256
Slots | 2
SNR(dB) | 10
Simulation assumption | value
 | 2
 | 2
 | 256
 | 2
SNR(dB) | 10
Notes: DnCNN: de-noise convolutional neural network

## Slide 13: Reception based on low dense pilot
Basic idea:
  NN based solution helps to get high BER performance with low dense pilot
Benefit: pilot dense can be reduced
Simulation assumption | value
Number of Tx antenna | 2
Number of Rx antenna | 2
Subcarriers | 256
Slots | 2
SNR(dB) | 10
Number of reference signals | 32 or 8
Simulation assumption | value
 | 2
 | 2
 | 256
 | 2
SNR(dB) | 10
 | 32 or 8

## Slide 14: Initial Proposal
To have a Rel-18 study item:
  To have a common understanding of AI/ML algorithm frame work without touching algorithm itself:
    For example which ML/AI category or architecture is applied for which use cases
    The potential impact on hardware and software e.g. computing power, storage capability etc.
  To take principle introduced in FS_NR_ENDC_data_collect for network optimization into account;
  To focus on link level use cases including:
    Technical justification, feasibility and potential performance enhancement compared to benchmark of 5G network
    To conclude which ones are valuable to be specified
  To investigate potential standard impact case by case including but not limited to:
    Output and input of ML/AI algorithm
    Information exchanged over Uu and/or network interface
Note: It is assumed both network node and UE can be ML/AI model training or inference host