## Slide 1
Discussion on testability of NR 52.6-71 GHz RAN4
Core requirements
3GPP TSG RAN Meeting #91e RP-210314
Electronic Meeting, 16th– 26th March, 2021
Agenda Item: 9.7.2
Document for: Discussion & Decision

## Slide 2
  In RAN#90e meeting, the testability issue of 60GHz was discussed in [90E][43][60GHz_OTA] email thread, the summary is captured in RP-202873.
  Several options on how to treat 60GHz OTA testability in Rel-17 were discussed, but no conclusion:
    Option 1: Include NR 52.6-71GHz UE OTA test methods objectives in the scope of Rel-17 NR FR2 Test Methods Enhancements SI (FS_FR2_enhTestMethods)
    Option 2: Include NR 52.6-71GHz UE OTA test methods objectives in the scope of a new “umbrella” SI on OTA topics (if such new item is approved)
    Option 3: Include NR 52.6-71GHz UE OTA test methods objectives in the scope of Rel-17 NR 52.6-71GHz WI
    Option 4: RAN4 define the core requirements for 52.6-71GHz and leave the test related issues to RAN5 WI, co-ordination between RAN4 and RAN5 can be triggered by LS if needed
    Other options are not precluded
  The timeline schedule of study NR 52.6-71GHz UE OTA test methods was discussed with several options:
    Option A: Wait until the NR 52.6-71 GHz RF Core requirements framework is stable
    Option B: Start work in parallel with NR 52.6-71 GHz RF Core requirements definition
    Other options are not precluded
  In RAN4#98e meeting, the Testability aspect on 60GHz was also discussed, the initial agreement was captured in R4-2103258
    FR2 OTA method as baseline, and RAN4 further identifies differences compared to FR2
Background

## Slide 3
  During Rel-15 timeline, the FR2 UE test methods were studied with FR2 RF Core requirements definition.
    Proposal1: The testability study of 60GHz should be started work in parallel with NR 52.6-71 GHz RF Core requirements definition.
  Several test methods have been defined and preliminary MU assessment was done for some high priority requirements (e.g. MOP and REFSENS), but the testability issue was not discussed case by case for all the FR2 RF requirement in RAN4, then there are few issues raised:
    Even RAN4 already defines the minimum RF requirements for FR2, some requirements still need additional 0~20dB relaxation to make it testable (e.g. Transmit OFF power, Maximum input power, Receiver spurious emissions, etc. ), due to the physical limitation of test systems;
    By now, some requirements are still deemed untestable;
  Therefore, for FR2 UE RF requirements, the testability issue has great impacts on final requirements, additional relaxation of core requirement or untestable or not should be identified during testability study.
    Proposal 2: For 60GHz, the testability issue should be studied comprehensively with RF Core requirements definition in RAN4.
  Clear work split have been agreed between RAN4 and RAN5 that RAN4 focus on OTA requirements and test methods, RAN5 focus on TT and test cases.
    Proposal 3: For 60GHz, the potential requirement relaxation on top of minimum requirement due to testability issue should be defined in RAN4.
Views on RAN4 FR2 requirements and test methods

## Slide 4
  During Rel-16 timeline, the FR2 test methods enhancement SI developed the enhanced solutions to ease the FR2 testability issue, some relaxation have been removed or reduced.
  The testability of n262 is under discussion within the FR2 enhanced test method SI, progress has been made on testability of 49GHz. Based on the outcome of 60GHz SI, large bandwidth of single carrier (e.g. ≥2GHz) would be supported, then the challenge of test methods is dramatically increased.
    Proposal4: The defined FR2 test methods should be baseline for 60GHz, but whether 60GHz RF requirements are testable or not needs further study.
  The efforts of test group should be gathered to resolve the challenging testability issues efficiently.
    Proposal 5: Including NR 52.6-71GHz UE OTA test methods objectives in the scope of Rel-17 NR FR2 Test Methods Enhancements SI could gather the efforts of test group.
Views on RAN4 FR2 requirements and test methods

## Slide 5
  Proposal1: The testability study of 60GHz should be started work in parallel with NR 52.6-71 GHz RF Core requirements definition.
  Proposal 2: For 60GHz, the testability issue should be studied comprehensively with RF Core requirements definition in RAN4.
  Proposal 3: For 60GHz, the potential requirement relaxation on top of minimum requirement due to testability issue should be defined in RAN4.
  Proposal4: The defined FR2 test methods should be baseline for 60GHz, but whether 60GHz RF requirements are testable or not needs further study.
  Proposal 5: Including NR 52.6-71GHz UE OTA test methods objectives in the scope of Rel-17 NR FR2 Test Methods Enhancements SI could gather the efforts of test group.
Proposals summary for 60GHz testability