## Slide 1: Motivation Introducing Rail Mobile Radio allocated spectrum
Ingo Wendler (UIC)
Contact: ingo.wendler@sbb.ch
RP-210352

## Slide 2: Background
Today Rail Communication already uses 3GPP technology and would like to continue this with the Future Railway Mobile Communication System (FRMCS), especially for reasons of interoperability. With FRMCS, 3GPP broadband technology will be used for the first time, for whose operation in Europe spectrum in the 900MHz and 1900MHz range, as Railway Mobile Radio (RMR), was allocated by CEPT for non-safety services. Only certain applications, e.g., ETCS, processed via Rail Mobile Radio are classified as relevant to safety.
In detail, these are the spectrum ranges:
2x5.6 MHz 874.4-880MHz / 919.4-925MHz (FDD)
1x10 MHz 1900-1910MHz (TDD).

## Slide 3: Targets
The spectrum ranges mentioned are to be understood for rail operational purposes under different boundary conditions like train speed up to 500km/h, low latency and reliability requirements in accordance with 3GPP TS 22.289.
For the use of spectrum, ECC Decision (20)02 “Harmonized use of the paired frequency bands 874.4-880.0 MHz and 919.4-925.0 MHz and of the unpaired frequency band 1900-1910 MHz for Railway Mobile Radio (RMR)” applies. https://docdb.cept.org/document/16736
UIC, as a representative of the railways, aims to make the spectrum ranges (900MHz/1900MHz) available for the use of 3GPP technology.

## Slide 4: Corresponding documents
RP-210356 Rail Mobile Radio 900MHz spectrum
RP-210357 Rail Mobile Radio 1900MHz spectrum