## Slide 1: Scope of Rel-17 Sidelink Relay WI
CMCC

## Slide 2: Motivation of Sidelink relay
Further explore coverage extension for sidelink-based communication
  Support UE out of uu coverage access to network with UE in coverage as Sidelink relay
  Support UE communication with other UE without proximity reachability
Ensure power efficiency for User Equipments
  Substitute PC5 connection for uu link , the UE-to-Network Relay enables power saving for the Remote UE

## Slide 3: Conclusion of sidelink relay SI
  In this study, both Layer-2 based Relay architecture and Layer-3 based Relay architecture have been found feasible.
  L2 Relay meets all of the objectives of the SID.
  The standards impact of L2 is principally in RAN and the standards impact of L3 is principally in SA. RAN2 strives for minimum specification impact.
  RAN2 recommends both L2 and L3 UE to NW and UE to UE relay can proceed to normative work.

## Slide 4: Sidelink relay from Operator perspective
L3 sidelink relay imposes some challenges on network deployment
    Sidelink relay is primarily a RAN feature for coverage enhancement and is deployed on demand for certain regions.
    The standards impact of L3 relay is principally in core network. Once operators plans to introduce the sidelink relay feature in certain areas, large-scale upgrade of the core network cannot be avoided if only L3 sidelink relay is supported by the standard, which is not friendly for operators.
L2 relay is more flexible in network deployment
  The standards impact of L2 Relay is mostly in RAN
  L2 sidelink relay works well in resource control, load balance, QoS management and mobility, which is valued by operators.

## Slide 5: Proposals
Following RAN2 agreements for Sidelink relay SI, i.e., both L2 and L3 UE to NW and UE to UE relay proceed to normative work, with minimum specification impact.
U2N sidelink relay should be prioritized.

## Slide 6: Proposed scope of sidelink relay WI
  Specify mechanism(s) for Layer-2 (L2) Sidelink-based UE-to-Network Relay,
  Relay discovery and (re)selection [RAN2, RAN4];
  Relay and Remote UE authorization [RAN3];
  Service continuity [RAN2, RAN3];
  Adaptation layer design [RAN2];
  QoS management [RAN2];
  Control Plane procedure design, including RRC connection management, system information delivery, paging mechanism and access control for Remote UE, to enable L2 Relay [RAN2];

## Slide 7: Proposed scope of sidelink relay WI
Specify mechanism(s) for Layer-3 (L3) Sidelink-based UE-to-Network Relay
  Relay discovery and (re)selection [RAN2, RAN4];
  Relay and Remote UE authorization [RAN3];
  QoS management [RAN2];