## Slide 1: Rel-17 Sidelink Relay Motivation
MediaTek Inc., Interdigital, Futurewei, Apple, Huawei, HiSilicon, Convida Wireless, Sony, Lenovo, Motorola Mobility, China Unicom, China Telecom, Xiaomi, ZTE, Fujitsu, Spreadtrum, Philips

## Slide 2: The case for relaying
The need of coverage extension
  As demonstrated in the coverage enhancements SI
  Other existing/proposed solutions: IAB, small cells, and repeaters
The need to ensure power efficiency for User Equipments
Channel enhancements offer some benefit (a few dB)
This situation was a significant motivation for the sidelink relay SI
  Sidelink relay does not require planning (doesn’t radiate like a base station)
  Coverage extension can be achieved with a customer-managed device (less operator effort/expense)
Essential enablers for sidelink relaying
  Trust of the communication path
  Service continuity
  QoS of relayed services

## Slide 3: Requirements of U2N relaying for coverage extension
Coverage extension is largely a commercial service
  Also used for public safety, but many users will be commercial customers
  The relay may not be owned by the end user (e.g. coffee shop hotspot)
Service requirements for commercial usage
  Reliable, timely communication (basic requirement)
  Good performance required for commercial usage
  Access to the 3GPP ecosystem of services, with QoS
  Service continuity
    Critical requirement: Service must not be interrupted when switching between direct and indirect paths
    Secondary requirement: Minimal disruption to the data flow, i.e. lossless handover preferable
  Security equivalent to direct Uu service (i.e. encryption and integrity)
    Relay UE may not be a trusted node from the perspective of the remote UE

## Slide 4: Findings of the relaying SI for U2N
 | L2 | L3 basic | L3+N3IWF | Comment
Data communication | Yes | Yes | Yes | Some latency and overhead concern with N3IWF resulting in performance degradation (more network hops, additional headers)
Service access with QoS | Yes | Yes | Yes | PDB split is handled differently in L2 and L3 architectures L2 QoS can be flexibly tailored to the AS conditions on sidelink and Uu, but L3 cannot.
End-to-end security | Yes (PDCP) | No | Yes (IPsec) | 
Service continuity | Yes (handover) | No | Partial (no lossless handover) | 
Both the L2 and L3 solutions can meet service requirements, but L3 requires N3IWF
  only L2 would be able to provide lossless service continuity
  Performance concerns with N3IWF: overhead, latency, likelihood of deployment
Layer 2 and layer 3 relay architectures are both deemed feasible and recommended for normative work

## Slide 5: Recommended way forward
Any specified U2N/U2U relay architecture should be suitable for commercial use
  Otherwise there is a risk of a paper standard
L2 solution should be specified

## Slide 6: Proposed WI objectives
Specify a layer 2 relaying architecture to support the SA requirements for both sidelink-based UE-to-Network relay and UE-to-UE relay:
  Control Plane procedures
  Adaptation layer and other user plane protocol aspects to support QoS and End-to-end security for relaying connection
  Service continuity for UE-to-Network relay
  QoS for relaying functionality
  Relay/remote UE authorisation
Specify criteria and procedures for relay (re)selection
Specify procedures for support of discovery operations for sidelink relaying