## Slide 1: Introduction of event-based trigger for LTE MDT logging
KDDI Corporation, TIM, Samsung
3GPP TSG RAN Meeting #91e RP-210736
Electronic Meeting, March 16-26, 2021 (revision of RP-210277)

## Slide 2: 1. Background : Not treated in RAN2
We had submitted the contribution [1][2][3][4][5] to last RAN2 meeting, those contributions propose to introduce MDT event trigger for LTE. However, our proposal was not treated. We think that our proposal is beneficial for operators and we try to progress the discussion in this contribution.

## Slide 3: 2. Benefit : Improve accuracy and efficiency
The following figure shows how the MDT logging works in LTE and NR. In NR, entries are logged every interval (t3) and the immediate timing of transition from any cell selection to the camped normally (C1 and C2). On the other hand, in LTE, since outofcoverage is not supported, so entries are logged only at the intervals. In LTE, both anycellselection detected true/false are captured (t1, t2, t3, t4, t5, t6), so entries can easily become huge and full, this results in frequent sending UE information Request to UE to get the logged information. So, we propose to introduce outofcoverage logging to LTE, so that we can improve its accuracy and efficiency (less logging data).

## Slide 4: 3. Proposal : Modify Rel-17 SON/MDT WID
RAN agree to add the following objective to Rel-17 SON/MDT WID[6]
  The event triggered LTE MDT logging function, at least for out-of-coverage detection trigger.

## Slide 5: 4. References
[1] R2-2101808 Introduction of event-based trigger for LTE MDT logging KDDI Corporation, CMCC, Samsung
[2] R2-2100818 draftCR Introduction of event-based trigger for LTE MDT logging KDDI Corporation Rel-16 36.331
[3] R2-2100819 draftCR Introduction of event-based trigger for LTE MDT logging KDDI Corporation Rel-17 36.331
[4] R2-2100821 draftCR Introduction of event-based trigger for LTE MDT logging KDDI Corporation Rel-16 37.320
[5] R2-2100823 draftCR Introduction of event-based trigger for LTE MDT logging KDDI Corporation Rel-17 37.320
[6] RP-193255 New WID on enhancement of data collection for SON/MDT in NR CMCC