3GPP TSG RAN Meeting #91-e	RP-210xxx

# Electronic Meeting, March 16 - 26, 2021

Source:	Moderator (Huawei)

Title:	[91E][15][Pi2_BPSK_SI] initial round summary

Agenda item:	9.1.5

Document for:	Discussion and decision

# Introduction

The study item proposal in RP-210436 provides the following objectives:

The objective of this study is to evaluate the feasibility of increasing the UE’s uplink power in TDD bands for pi/2 BPSK modulation assuming use of existing UE power classes as indicated per band or band combination.

- Identify achievable UE Tx power for pi/2 BPSK with the pulse shaping filter studied in this study item.

- Evaluate SAR-related duty-cycle restrictions and reporting mechanisms

- Identify shaping filter characteristics necessary to enable the new power capability while ensuring good and robust BS receiver performance.

  - Justify specification of a pulse shaping filter for this new identified UE power capability if it differs from filter impulse response specification in TS38.101-1 clause 6.4.2.4.1.E

  - Evaluate possible pulse shaping filter requirement applicable to the identified new UE power capability if achievable

  - Identify if necessary changes are needed to EVM equalizer flatness mask requirements to capture necessary filter shaping. Changes to the existing 14 dB p-p baseline to be assessed in relation to any potential gains in UL link performance while still ensuring robust BS receiver performance for all UEs in a cell.

The objectives are applicable to FR1.

The initial round of this email discussion will aim to clarify questions on the proposed objectives, and to discuss the associated timeplan until TSG#94. Since the proponents of RP-210436 have not provided the required TU budget in an excel sheet, I would first like to ask the proponent to provide the planned TU budget (how may TU per RAN4 meeting/session is requested to complete the proposed study until TSG#94?).

Templates for collecting views on the two questions are provided in the following section. Please provide your comments before Tuesday 11:59h UTC. Thank you.

# Initial Round

Question #1: please provide your comments on objectives 1, 2, and 3 of RP-210436

Companies are invited to provide the comments below.

| Company | Comments |
| --- | --- |

Question #2: please provide your comments on the proposed timeplan (completion at TSG#94, TU budget)

Companies are invited to provide the comments below.

| Company | Comments |
| --- | --- |

# Conclusions of initial round

TBD

# References

- RP-210436, New SID: Optimizations of pi/2 BPSK uplink power in NR, Qualcomm

# Contact Persons

Please add your contact information when responding to the discussion. Thank you.

| Company | Contact person (name, email) |
| --- | --- |