## Slide 1
On duplex evolution
RP-213267
3GPP TSG RAN Meeting #94-e
Electronic Meeting, Dec 6 – 17, 2021
Document for: Discussion and Decision
Agenda Item: 8A.1
Source: vivo

## Slide 2
Duplex evolution is an promising study area in Rel-18
  Based on the previous discussion, Rel-18 duplex evolution study will focus on the more flexible spectrum utilization at the NW side, i.e.
      Duplex enhancement at the gNB side (sub-band non-overlapping, and dynamic TDD)
      Half duplex operation at the UE side
      No restriction on frequency ranges
  Draft SID is available in RP-212707 as the outcome of previous discussion
UE impact due to Rel-18 duplex evolution should be minimized
  Legacy UE should be able to work within a NW or cell operating enhanced duplexing methods
  No UE hardware/RF changes is highly preferable
    Existing UE RF requirements are assumed to evaluate the performance impact due to CLI at the UE side
      For adjacent channel (i.e. inter-operator) CLI study, existing UE ACLR (Adjacent Channel Leakage Ratio) at Tx side, ACS (Adjacent Channel Selectivity) at Rx side are assumed.
      For inter sub-band (i.e. intra-operator) CLI study, existing UE IBE (In-band Emission) at Tx side, IBB (In-band Blocking) at Rx side are assumed
    However, some signaling enhancements can be introduced for advanced UEs to work more efficiently in the NW or cell operating enhanced duplexing methods
  Accordingly, the SID revision is provided in the next page.
On duplex evolution

## Slide 3
The detailed objectives are as follows:
  Identify applicable and relevant deployment scenarios and use cases (RAN1).
  Develop evaluation methodology for duplex enhancement (RAN1).
  Study the subband non-overlapping full duplex and potential enhancements on dynamic/flexible TDD.
    Identify possible schemes and evaluate their feasibility and performances (RAN1).
    Study inter-gNB and inter-UE CLI handling and identify solutions to manage them (RAN1).
      Study their impacts on inter-gNB interfaces if needed (RAN3).
      Consider intra-subband CLI and inter-subband CLI in case of the subband non-overlapping full duplex.
    Study the performance of the identified schemes as well as the impact on legacy operation assuming their co-existence in co-channel and adjacent channels (RAN1).
    Study the impact on RF requirements considering the self-interference, the inter-subband CLI, and the inter-operator CLI at gNB and the inter-subband CLI and inter-operator CLI at UE (RAN4).
      Note: The existing UE RF requirement is assumed in the study
    Study the impact on RF requirements considering adjacent-channel co-existence with the legacy operation (RAN4).
    RAN4 should be involved early to provide necessary information to RAN1 as needed and to study the feasibility aspects due to high impact in antenna/RF and algorithm design, which include antenna isolation, TX IM suppression in the RX part, filtering and digital interference suppression.
  Summarize the regulatory aspects that have to be considered for deploying the identified duplex enhancements in TDD unpaired spectrum (RAN4).
Note: For potential enhancements on dynamic/flexible TDD, utilize the outcome of discussion in Rel-15 and Rel-16 while avoiding the repetition of the same discussion.
Proposed SID revision