## Slide 1: Motivation for BS EMC Test Simplification
Ericsson
3GPP TSG RAN Meeting # 94-e
Electronic meeting, December 6-17, 2021
Agenda item: 8.6.4
Document for: Information
RP-213425

## Slide 2: Background: BS EMC
Current testing of EMC requirements as specified in TS 37.113 or TS 37.114 (AAS BS, which is part of the MSR standard) is increasingly complex and considers many test configurations, due to various possible RAT combinations.
The TCs for MSR BS are defined in TS 37.141 and include 19 different capability sets (including 3 of single mode condition: WCDMA, LTE and NB-IoT standalone), which cover the possible RAT combinations available in an MSR BS.
EMC is part of Rel-18 package with stable objectives [1]:
  Topic #6: EMC enhancement

## Slide 3: Justification: BS EMC
Currently the Capability Sets for MSR standard add a new combination when a new RATs comes in. Even though, this principle looks for an understandable follow up of technical developments, it might not be the most efficient way from an EMC testing perspective.
A simplification in the EMC testing could be achieved by considering the specificities of the EMC testing. An analysis of these characteristics might lead to alternatives such as the reduction in the number of RAT combinations defined in some Capability Sets, or the definition of Test Configurations and Capability Sets specifically devised for EMC tests.

## Slide 4: Objective of BS EMC: performance part of WI
Study phase (till RAN#X):
Investigate the potential following alternatives to achieve EMC test simplification (if any possible) considering both Emission and Immunity testing scenarios, with the priority on MSR/AAS BS.
  Considering Test Configurations
  Considering Capability sets
  A combination of Test configurations and Capability sets.
  NOTE 1: Potential testing optimizations for single RAT testing not to be excluded from the analysis.
  NOTE 2: Modification impacting RF Test Configurations and Capability sets are excluded from this WI. RF test specifications are not to be impacted.
Evaluate the potential gains (in terms of test reduction) of the alternatives considered in bullet 7 to achieve the EMC test simplification.
Implementation phase (based on study phase outcomes, till RAN#X+3):
Implement Emission testing simplifications in TS 37.113 and TS 37.114.
Implement Immunity testing simplifications in TS 37.113 and TS 37.114.
Apply adjustments of the existing RF capability sets and test configurations which are reused for EMC testing of MSR/AAS BS (according to the outcome of the study phase) considering both emission and immunity testing.
  NOTE: Modification impacting RF Test Configurations and Capability sets are excluded from this WI. RF test specifications are not to be impacted.
  Define the required adjustments (if any possible) to BS test configurations clause (i. e. clause 4.5 in TS 37.113, 4.4 in TS 37.114) considering both emission and immunity testing.
  NOTE 1: The starting point for the specification of capability sets and test configurations will be the existing ones defined in TS 37.141.
  NOTE 2: The purpose of this WID is not to change the existing limits for EMC testing.
  NOTE 3: for bullets 9 – 12, potential testing optimizations for single RAT testing not to be excluded.

## Slide 5: References
RP-212682, “Potential RAN4 enhancements”, RAN4 Chair (Huawei)