## Slide 1
Title: On BWP operation without bandwidth restriction
Agenda item: 9.11
Source: Samsung
Document for: Decision
3GPP TSG RAN Meeting #97-e
Electronic Meeting, September 12 – 16, 2022
RP-222241

## Slide 2: Background (1/3)
RAN2#117-e sent the LS [R2-2204009] with the following questions to RAN1 and RAN4:
The above two questions in the RAN2 LS came from the following:
  TS38.300 is describing that For BM/RLM/BFD operation on DL BWPs NOT containing the SSB associated to the initial DL BWP, CSI-based measurements are used.
  On the other hand, the current UE capability signaling allows the UE to indicate:
    It supports BWP operation without bandwidth restriction, i.e., configured DL BWP does not contain SSB associated to the initial DL BWP; and
    It does not support CSI-RS based RLM/BFD
    This indicates that the network may configure a DL BWP which does not contain SSB associated to the initial DL BWP, while not configuring CSI-RS for BM/RLM/BFD.
Question 1:
Whether it is a valid scenario in the standard to support the operation of BWP without SSB where the UE does not perform BM/RLM/BFD due to the lack of necessary reference signal (SSB and CSI-RS) in the active BWP.
Question 2:
If the answer to question 1 is that this is not valid, how should the UE perform BM/RLM/BFD when the active BWP does not contain SSB.

## Slide 3: Background (2/3)
RAN#96 agreed to give a guidance to the WGs as follows:
  To task the relevant Working Groups (RAN1, 2, 4) to make progress on their discussions related to the RAN2 LS in R2-2204009, aim to ensure that Feature Group 6-1a “bwp-WithoutRestriction” works in an early implementable form in R18, or, possible R17, and report progress to RAN#97.
According to the RAN#96 guidance, RAN1#110 discussed the RAN2 LS and concluded the following as captured in the reply LS to RAN/RAN2/RAN4 [R1-2208168];
RAN1 observation:
For a UE supporting RLM/BM/BFR using CSI-RS within active DL BWP, FG6-1a works without issue.
Conclusion:
To resolve the issue in the scenario described in the RAN2 LS (R2-2204009), RAN1 considers that SSB based RLM/BM/BFR that is outside active DL BWP is feasible and can be a solution
MediaTek, Samsung showed concern on the support of the scenario (active BWP without CSI-RS/SSB) mentioned in the RAN2 LS.

## Slide 4: Background (3/3)
According to the RAN#96 guidance, RAN4#104-e also discussed the RAN2 LS and sent the following reply LS to RAN/RAN1/RAN4 [R4-2214355]:
Question 1:
Whether it is a valid scenario in the standard to support the operation of BWP without SSB where the UE does not perform BM/RLM/BFD due to the lack of necessary reference signal (SSB and CSI-RS) in the active BWP.
Answer:
From the existing RAN4 specification point of view, it is not a valid scenario.
Question 2:
If the answer to question 1 is that this is not valid, how should the UE perform BM/RLM/BFD when the active BWP does not contain SSB.
Answer:
RAN4 has examined the Rel-15, Rel-16 and Rel-17 specs. The following possible solutions for the issue are identified.
- Perform BM/RLM/BFD based on CSI-RS within active BWP
o RAN4 has requirements to support BM/RLM/BFD based on CSI-RS within active BWP and no spec change is needed
- Following potential independent implementations/features requires either existing RAN4 requirements to be updated or new requirements to be developed.
o Perform BM/RLM/BFD based on SSB outside active BWP
    UE’s capability to operate using larger BW covering SSB outside active BWP, or a UE that is equipped with a separate RF chain
    BM/RLM/BFD on SSB outside BWP are performed with shared MG or NCSG for L3 measurement, or dedicated MG or NCSG for RLM/BFD/BM measurements.
o NCD-SSB approach which would work with existing UE hardware architectures (FG6-1) and be compatible with existing RAN4 specifications for
BM/RLM/BFD
o Note: RAN4 does not reach consensus on whether to work on the above items in Rel-17 including to update the existing RAN4 requirements or to
develop new requirements

## Slide 5: Discussions
RAN1 concluded that SSB based RLM/BM/BFR that is outside active DL BWP is feasible and can be a solution.
According to the RAN4 reply LS, however, the RAN1 solution seems to require either existing RAN4 requirements to be updated or new requirements to be developed.
Also, RAN4 indicated that RAN4 does not reach consensus on whether to work on the RAN1 solution in Rel-17 including to update the existing RAN4 requirements or to develop new requirements
On the other hand, RAN4 also indicated that the CSI-RS based solution can resolve the concerned scenario and it does not require additional specification change from RAN4.

## Slide 6: Proposal
Proposal: To ensure that FG 6-1a works, RAN guides RAN1, RAN2 and RAN4 to take the solution: Perform BM/RLM/BFD based on CSI-RS within active BWP

## Slide 7: Appendix
Index | Figure group | Components | Field name in TS38.331 | 
6-1 | Basic BWP operation with restriction | 1) 1 UE-specific RRC configured DL BWP per carrier 2) 1 UE-specific RRC configured UL BWP per carrier 3) RRC reconfiguration of any parameters related to BWP 4) BW of a UE-specific RRC configured BWP includes BW of CORESET#0 (if CORESET#0 is present) and SSB for PCell/PSCell (if configured) and BW of the UE-specific RRC configured BWP includes SSB for SCell if there is SSB on Scell | N.A. | Mandatory without capability signaling
6-1a | BWP operation without restriction on BW of BWP(s) | BW of UE-specific RRC configured BWP may not include BW of the CORESET#0 (if CORESET#0 is present) and SSB for PCell/PSCell (if configured) and BW of the UE-specific RRC configured BWP may not include SSB for Scell | bwp-WithoutRestriction | Optional with capability signaling
1-7 | CSI-RS based RLM | CSI-RS based RLM | csi-RS-RLM | Mandatory with capability signaling
1-8 | RLM based on a mix of SS block and CSI-RS signals within active BWP | RLM based on a mix of SS block and CSI-RS signals within active BWP | ssb-AndCSI-RS-RLM | Optional with capability signaling
2-31 | Beam failure recovery | 1) Maximal number of CSI-RS resources across all CCs for UE to monitor PDCCH quality 2) Maximal number of different SSBs across all CCs for UE to monitor PDCCH quality 3) Maximal number of different CSI-RS and/or SSB resources across all CCs for new beam identifications. | 1. maxNumberCSI-RS-BFD 2. maxNumberSSB-BFD 3. maxNumberCSI-RS-SSB-CBD | Mandatory with capability signaling for FR2 Optional with capability signaling for FR1