## Slide 1: Views on Rel-19 UL Coverage Enhancement
NTT DOCOMO, INC.
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - 16, 2023
Source: NTT DOCOMO, INC.
Agenda item: 5
Document for : Discussion
RWS-230258

## Slide 2: Multi-PRACH with different beams: Motivation
In Rel-18, multiple PRACH transmissions with same Tx beam is supported.
Multiple PRACH transmissions with different Tx beams is NOT supported in Rel-18.
Potential benefit of multiple PRACH transmissions with different Tx beams:
  Multiple PRACH transmissions with different Tx beams can provide performance gain for some cases, especially when UE has no prior knowledge about the best narrow UL Tx beam.
  Best UL Tx beam identification for Msg3 PUSCH is possible, which is beneficial for Msg 3 PUSCH coverage.
View:
  With small standardization effort, Rel-19 can consider specifying multi-PRACH transmissions with different beams
    Potential objectives are captured in the next slide
Rep#1
Rep#2
Rep#3
Rep#4
Msg 1
Msg 1
Msg 1
Msg 1
RAR
RAR window
Msg 3
Best UL Tx beam for Msg 3

## Slide 3: Multi-PRACH with different beams: Objective
Supported case:
  Multiple PRACH transmissions with different Tx beams associated with same SSB/CSI-RS
Detail design:
  PRACH resource
    Study whether Rel-18 multi-PRACH with the same beam is reused or not.
  Determination for number of PRACH transmissions
    Study whether Rel-18 multi-PRACH with the same beam is reused or not.
  RAR monitoring
    Study whether Rel-18 multi-PRACH with the same beam is reused or not.
  Indication of the best UL Tx beam for Msg 3 PUSCH transmission
    Specify the method to inform UE of the best beam for Msg3 PUSCH transmission
Leading WGs: RAN1 and RAN2

## Slide 4: Power domain enhancement: P-MPR reporting
Motivation
  UE Tx power availability is important to determine proper UL scheduling
    Legacy PHR can report PCMAX for the corresponding band, which plays an important role
  With high-power UE being deployed, it is expected that UEs adjust its maximum transmit power in a dynamic manner to e.g., compliant with SAR
    There are multiple approaches that UE can implement for this purpose, e.g., using ΔPPowerClass, or P-MPR
  Such power adjustment cannot be expected for NR based on the existing PH reporting, e.g.,
    Although ΔPPowerClass reporting can be supported in Rel-18, P-MPR reporting for FR1 is not supported until Rel-18
    Even if ΔPPowerClass is supported, it is likely to be as instantaneous information. No information for future power availability is to be supported
View: Specify enhancements by which NW-side awareness on UE power availability is improved, e.g.,
  Specify P-MPR reporting for FR1 in Rel-19
    Additional restriction of the reported value can also be studied (e.g., when the reported P-MPR is expired)
  Study, and if needed specify, ΔPPowerClass and P-MPR reporting with additional information, e.g.,
    Timing when the reported ΔPPowerClass and P-MPR are expired
Leading WGs: RAN4, RAN1 and RAN2

## Slide 5: PHY channel coverage enhancement: Msg5
Motivation:
  Until Rel-18, repetition-based coverage enhancements are (to be) specified
    PUSCH after RRC connection
    Msg3 PUSCH
    PUCCH
    PRACH
  Meanwhile, “Msg5 PUSCH repetition” doesn’t support repetition
    “Msg5 PUSCH” is a PUSCH after Msg3 PUSCH and before reception of dedicated PUSCH config
  Without repetition, Msg5 PUSCH can be a significant bottleneck, especially for NTN operation
View
  (If not supported in R18,) specify repetition for PUSCH after Msg3 PUSCH and before reception of dedicated PUSCH config
Leading WGs: RAN1