## Slide 1
Clarification of CSI reporting (Rel.15)
Agenda Item: 7.1
Source: Ericsson
Document for: Discussion, Agreement
3GPP TSG-RAN WG1 Meeting #110-bis-e Tdoc R1-2208730
Online, October 10th – 19th, 2022

## Slide 2: Background and aim
Ericsson product developers observed that different UE chipset vendors interprets part of the spec related to CSI reporting differently
  Related to a combination of CSI-ReportingBand and Part 2 of the CSI report
With mismatched gNB-UE side interpretation respectively, the CSI report contains nonsense
RAN1 needs to clarify the intention of the spec during RAN1#110bis-e

## Slide 3: Relevant spec text from 38.212 Mapping order for subband reporting
Mapping order for CSI part 2 follows:
  Subband diff CQI for 2nd TB for all even subbands
  PMI of all even subbands
  Subband diff CQI for 2nd TB for all odd subbands
  PMI of all odd subbands

## Slide 4: Relevant spec text from 38.331 csi-ReportingBand
csi-ReportingBand
Indicates a contiguous or non-contiguous subset of subbands in the bandwidth part which CSI shall be reported for. Each bit in the bit-string represents one subband. The right-most bit in the bit string represents the lowest subband in the BWP. The choice determines the number of subbands (subbands3 for 3 subbands, subbands4 for 4 subbands, and so on) (see TS 38.214 [19], clause 5.2.1.4). This field is absent if there are less than 24 PRBs (no sub band) and present otherwise (see TS 38.214 [19], clause 5.2.1.4).
Note: Subbands for given CSI report n indicated by the higher layer parameter csi-ReportingBand are numbered continuously in the increasing order with the lowest subband of csi-ReportingBand as subband 0.

## Slide 5: Interpretation 1 of the spec for four cases
  Lowest subband with a value ‘1’ in csi-ReportingBand is labeled subband 0

## Slide 6: Interpretation 2 of the spec for four cases
  Lowest subband in csi-ReportingBand is labeled subband 0
Different from Interpretation 1
Different from Interpretation 1
Different from Interpretation 1

## Slide 7: Overview of company views
Offline discussions on Option 1 and 2:
Company | Vendor type | Interpretation
1 | UE | 1
2 | UE | 1
3 | UE | 2
4 | Network | 1

## Slide 8: Proposed Resolution
Agree on the Option to use
Clarify with a Rel.17 CR with the agreed option

## Slide 9: Possible CR assuming Interpretation 1 is adopted (38.212)
CSI report number | CSI fields
CSI report #n CSI part 1 | CRI as in Tables 6.3.1.1.2-3/4, if reported
 | Rank Indicator as in Tables 6.3.1.1.2-3/4/5, if reported
 | Wideband CQI for the first TB as in Tables 6.3.1.1.2-3/4/5, if reported
 | Subband differential CQI for the first TB with increasing order of subband number as in Tables 6.3.1.1.2-3/4/5, if reported
 | Indicator of the number of non-zero wideband amplitude coefficients for layer 0 as in Table 6.3.1.1.2-5, if reported
 | Indicator of the number of non-zero wideband amplitude coefficients for layer 1 as in Table 6.3.1.1.2-5 (if the rank according to the reported RI is equal to one, this field is set to all zeros), if 2-layer PMI reporting is allowed according to the rank restriction in Clauses 5.2.2.2.3 and 5.2.2.2.4 [6, TS 38.214] and if reported
Note: Subbands for given CSI report n indicated by the higher layer parameter csi-ReportingBand are numbered continuously in the increasing order with the lowest subband of csi-ReportingBand with value set to ‘1’ as subband 0. | 
CSI report number | CSI fields
CSI report #n CSI part 1 | CRI as in Tables 6.3.1.1.2-3/4, if reported
 | Rank Indicator as in Tables 6.3.1.1.2-3/4/5, if reported
 | Wideband CQI for the first TB as in Tables 6.3.1.1.2-3/4/5, if reported
 | Subband differential CQI for the first TB with increasing order of subband number as in Tables 6.3.1.1.2-3/4/5, if reported
Note: Subbands for given CSI report n indicated by the higher layer parameter csi-ReportingBand are numbered continuously in the increasing order with the lowest subband of csi-ReportingBand with value set to ‘1’ as subband 0. | 

## Slide 10: Possible CR assuming Interpretation 2 is adopted (38.212)
CSI report number | CSI fields
CSI report #n CSI part 1 | CRI as in Tables 6.3.1.1.2-3/4, if reported
 | Rank Indicator as in Tables 6.3.1.1.2-3/4/5, if reported
 | Wideband CQI for the first TB as in Tables 6.3.1.1.2-3/4/5, if reported
 | Subband differential CQI for the first TB with increasing order of subband number as in Tables 6.3.1.1.2-3/4/5, if reported
 | Indicator of the number of non-zero wideband amplitude coefficients for layer 0 as in Table 6.3.1.1.2-5, if reported
 | Indicator of the number of non-zero wideband amplitude coefficients for layer 1 as in Table 6.3.1.1.2-5 (if the rank according to the reported RI is equal to one, this field is set to all zeros), if 2-layer PMI reporting is allowed according to the rank restriction in Clauses 5.2.2.2.3 and 5.2.2.2.4 [6, TS 38.214] and if reported
Note: Subbands for given CSI report n indicated by the higher layer parameter csi-ReportingBand are numbered continuously in the increasing order with the lowest subband corresponding to the right-most bit of csi-ReportingBand labelled as subband 0. | 
CSI report number | CSI fields
CSI report #n CSI part 1 | CRI as in Tables 6.3.1.1.2-3/4, if reported
 | Rank Indicator as in Tables 6.3.1.1.2-3/4/5, if reported
 | Wideband CQI for the first TB as in Tables 6.3.1.1.2-3/4/5, if reported
 | Subband differential CQI for the first TB with increasing order of subband number as in Tables 6.3.1.1.2-3/4/5, if reported
Note: Subbands for given CSI report n indicated by the higher layer parameter csi-ReportingBand are numbered continuously in the increasing order with the lowest subband corresponding to the right-most bit of csi-ReportingBand labelled as subband 0. |