## Slide 1: Power requirement for WUS
RAN1 111e Meeting
TDoc: R1-2211325

## Slide 2: Ultra-Low Power (ULP) Receiver Survey
Total of 210 receivers published in major IEEE circuits conferences and journals from 2005 to present
  All are measurement results from fabricated receiver chips
Includes active power, sensitivity, data rate, modulation, RF band, SIR, etc.
Link: https://wics.engin.umich.edu/ultra-low-power-radio-survey/
  Or search for: low power radio survey

## Slide 3: Receiver Active Power vs. Sensitivity Normalized to 1kb/s
Key Takeaways
Receiver active power trades off with sensitivity: 10x Power : 20dB Sens.
For sensitivity <-100dBm, power generally >20µW
All nanoWatt receivers are rectifier-first architectures

## Slide 4: Active Power vs. Signal to Interference Ratio (SIR)
Note:
Only 69 of 210 papers report SIR
All nanoWatt receivers are rectifier-first architectures
>100µW enables RF LO and mixer-first architecture == superior selectivity

## Slide 5: Histogram of modulation used for each ULP receiver

## Slide 6: Histogram of modulation used for each ULP receiver
OOK / PPM
OOK is used for <100µW

## Slide 7: Histogram of modulation used for each ULP receiver
FSK
FSK uses RF LO, power
requirement >100µW

## Slide 8: Histogram of modulation used for each ULP receiver
PSK
PSK requires RF PLL with
superior phase noise:
Power >1mW

## Slide 9: Summary
Agreed power requirement for WUS is relative to sleep power of the main radio
Absolute power of 100uW, 1mW, and 10mW will have very different impact on the applicable WUR architecture and other specs
We should agree on a baseline for the relative power, or narrow it to a small range of power, in order to down-select modulation and WUR architecture
Proposal 1: 1 unit of power is in the range of 3mW to 5mW