## Slide 1: FL plan on L1 enhancements for LTM at RAN1#112
3GPP TSG RAN WG1 #112 R1-2300145
Athens, Greece, February 27th – March 3rd, 2023
Document For: Information
Agenda item 9.12.1
Source: Moderator (Fujitsu)

## Slide 2: Overview

## Slide 3: Goal of RAN1#112(Feb)
RAN1#112 (Feb)
  In RAN1#110b-e and RAN1#111, most of the discussion time was spent to draw an overall picture of Rel-18 LTM, and we were able to make important decisions, e.g. TCI framework
  It is expected to resolve remaining important topics (please see next slide for more details)

## Slide 4: Detailed initial plan for each meeting
Meeting No | Key issues
No bis meeting | 
RAN1#112 | Down-selection of the measurement configuration options Detailed contents of measurement reporting Further clarification on the UE procedure around the reception of LTM cell switch command Introduction of L1-SINR Introduction of CSI-RS for L1 measurement
RAN#99(Mar) | TBD
The plan for RAN1#112 is subject to further update based on companies’ contributions

## Slide 5: RAN1 agreements and next action
FL plans for RAN1#112

## Slide 6: L1 measurement: L1 Intra-freq measurement
FL recommendation is that RAN1 use the same definition as RAN4 for SSB based L1 measurement, i.e. same as L3 measurement
  A measurement is defined as a SSB based intra-frequency L1 measurement provided the center frequency and SCS of the SSB of the neighbor cell is the same as SSB of the serving cell indicated in ServingCellConfigCommon
Decision on the use of CSI-RS is necessary, see this slide
  RAN1 needs to inform our decision (if CSI-RS based L1 measurement is supported) to accelerate the RAN4 discussion
RAN1 needs to wait for further RAN4 reply on the relaxation in terms of SFN offset alignment, BWP setting and Rx timing difference
[Conclusion at RAN1#110b-e]
Agreement
For Rel-18 L1/L2 mobility, L1 intra-frequency measurement for candidate cell is supported
  At least the following aspects are for RAN1 further study:
    RAN1 assumes Rel-17 ICBM CSI measurement as starting point.
    Whether and how to apply relaxation for the restrictions imposed on the Rel-17 intra-frequency L1 non-serving cell measurement defined in 9.13.2 of TS38.133, where RAN4 impact is foreseen, e.g.
      SFN offset alignment compared with serving cell
      BWP setting, i.e. non-serving cell SSB should be covered by serving cell active BWP
      Introduction of symbol level gap or SMTC for larger Rx timing difference (i.e. larger than CP length)
    Commonality with intra-frequency L3 measurement
    Commonality with L1 inter-frequency measurement for measurement configuration
Send an LS to RAN4 (CC RAN2)
  RAN1 to ask RAN4 if the restriction on e.g., SFN offset alignment, BWP setting and Rx timing difference, etc, described in 9.13.2 of TS38.133 for intra-frequency L1 non-serving measurement can be relaxed or not.
  RAN1 assumes Rel-17 ICBM CSI measurement as starting point.
  [Conclusion at RAN1#111]
  No discussion, wait for RAN4 LS
No immediate RAN1 discussion/decision is necessary, wait for RAN4 further reply LS

## Slide 7: L1 measurement: L1 Inter-freq measurement
According to the RAN4 reply LS, FL’s understanding is that the following scenarios can be treated as intra-frequency irrespective of the status of BWP activation (but some conditions exist)
  The frequency of the measured RS not covered by any of the active BWPs of SpCell and Scells configured for a UE, but covered by some of the configured BWPs of SpCell and Scells configured for a UE.
  The frequency of the measured RS not covered by any of the configured BWPs of SpCell and Scells configured for a UE
RAN1 needs more discussion on the behaviour of the L1 measurement for deactivated cells and the intra-frequency candidate cells linked with the deactivated cells.
[Conclusion at RAN1#110b-e]
Agreement
For Rel-18 L1/L2 mobility, further study the potential RAN1 spec impact of L1 inter-frequency measurement
  The definition and scenarios of L1 inter-frequency measurement is determined by RAN4, and RAN1 assumes at least the following until receiving their confirmation
    The scenarios not included in intra-frequency are regarded as inter-frequency, which includes at least the following scenarios:
      The frequency of the measured RS not covered by any of the active BWPs of SpCell and Scells configured for a UE, but covered by some of the configured BWPs of SpCell and Scells configured for a UE.
      The frequency of the measured RS not covered by any of the configured BWPs of SpCell and Scells configured for a UE
  At least the following aspect is studied:
    Commonality with L1 intra-frequency measurement for measurement configuration
Send an LS to RAN4 (CC RAN2)
  RAN1 would like to confirm our understanding that the supported scenarios not included in intra-frequency are regarded as inter-frequency, which includes at least the following scenarios:
    The frequency of the measured RS not covered by any of the active BWPs of SpCell and Scells configured for a UE, but covered by some of the configured BWPs of SpCell and Scells configured for a UE.
    The frequency of the measured RS not covered by any of the configured BWPs of SpCell and Scells configured for a UE
  It is RAN1 understanding that the introduction of measurement gap and SMTC for L1 inter-frequency measurement, if any, is expected to be a RAN4 issue
  Note: this content is included in the LS agreed for intra-frequency L1 measurement
[Conclusion at RAN1#111]
Agreement
For Rel-18 LTM, L1 inter-frequency measurement is supported from RAN1 point of view.
No immediate RAN1 discussion/decision is necessary, wait for RAN4 further reply LS

## Slide 8: L1 measurement: Measurement RS
RAN1 need to decide if CSI-RS based L1 measurement is supported in Rel-18
  Considering the workload in RAN4, the decision should be done as early as possible
  FL plan is to conclude this issue in RAN1#112 (i.e. if no consensus, this topic will be deprioritized afterwards)
However, FL is not so positive to introduce CSI-RS based measurement in Rel-18
  Companies’ views are split according to the discussion so far
  CSI-RS based L1 measurement would be an optional feature for optimization, i.e. LTM will work without this functionality
[Conclusion at RAN1#110b-e]
Agreement
For Rel-18 L1/L2 mobility,
  SSB is supported for L1 intra-frequency measurement
  SSB is supported for L1 inter-frequency measurement if inter-frequency L1 measurements are supported
Further study the following L1 measurement RS for candidate cell
  CSI-RS for tracking, beam management, CSI and mobility, CSI-IM, which is for L1 intra-frequency and L1 inter-frequency (if supported)
[Conclusion at RAN1#111]
The FL proposal 1-4-v3 was not due to the lack of time during RAN1#111. Companies are encouraged to perform their analysis based on the latest proposal below:
For Rel-18 LTM,
  L1 measurement based on CSI-RS for beam management for candidate cells is supported for L1 intra-frequency measurement and L1 inter-frequency measurement if supported in RAN4
    The definition of intra- and inter- frequency for CSI-RS is defined in RAN4
    The CSI-RS is explicitly linked to a candidate cell
    Applicability to L1-RSRP and/or L1-SINR is separately discussed.
    FFS for the support of other CSI-RS types (i.e. tracking, CSI, mobility and CSI-IM).
Check the companies’ interest level for the introduction of CSI-RS from RAN1#112 contributions.
If the interest level is high, FL would suggest to agree on “Support CSI-RS for BM” for simplicity.
Otherwise, the discussion on measurement RS will be de-prioritized in RAN1#112

## Slide 9: L1 measurement: Measurement quantity
Introduction of L1-SINR (for both intra- and inter-frequency) needs to be decided in RAN1#112
  L1-SINR is a powerful tool for inter-frequency mobility, meanwhile the spec impacts to both RAN1 and RAN4 are not negligible
  Strong demand from operators is confirmed
  Meanwhile, the complexity and usefulness of L1 interference measurement (as an instantaneous value) needs more discussion
[Conclusion at RAN1#110b-e]
Agreement
For candidate cell measurement for Rel-18 L1/L2 mobility,
  L1-RSRP is supported for intra-frequency candidate cell measurement.
  Further study the following measurement quantities for candidate cell measurement
    L1-RSRP for inter-frequency (if supported)
    L1-SINR for intra-frequency and inter-frequency (if supported)
FFS: to assess the use case and the benefit of UL measurement instead of/in addition to DL L1 measurement, which includes:
  How the UL measurement result is used, e.g. handover decision
  Signals/channels used for UL measurement, e.g. SRS
  Spec impact including other WGs, e.g. definition of gNB measurement, interface to transfer RS configuration or measurement results
  Note: The next discussion will take place based on companies’ contribution in future meeting.
[Conclusion at RAN1#111]
Agreement
For candidate cell measurement for Rel-18 LTM,
  SSB based L1-RSRP is supported for intra-frequency measurement
  SSB based L1-RSRP is supported for inter-frequency measurement from RAN1 point of view
  FFS: L1-SINR, CSI-RS based L1-RSRP
FL plan is to spend some time on the technical discussion, and make RAN1 decision whether L1-SINR is supported for LTM in Rel-18 or not.
FL encourages constructive discussion, i.e. agreeing L1-SINR with solution mitigating the concern above.

## Slide 10: L1 measurement: Filtering for L1 measurement results
According to the discussion so far, FL expects that this discussion wouldn’t go to a positive direction.
Also, FL believes this functionality is an optional feature, i.e. LTM will work without this functionality
[Conclusion at RAN1#110b-e]
Postponed (FL proposal 1-6)
For Rel-18 L1/L2 mobility, [study the importance of mitigating the ping-pong issue for L1/L2 mobility, which is expected to align with RAN2. If important yes,] further study at least the following mitigation aspects:
  UE-based filtering to the L1 measurement results, where the definition of filtering includes:
    Time domain filtering: e.g. exact definition of time domain filtering, and/or
    Cell-level (spatial domain) filtering: e.g. how many beams are averaged, and/or how the beams are chosen.
  Applicability to L1-RSRP and L1-SINR (if supported)
  Applicability to intra-frequency and inter-frequency (if supported)
  Necessity to be specified in standard considering the presence of alternative implementation-based solutions, e.g. gNB-based filtering and/or L3 measurement (when involved)
[Conclusion at RAN1#111]
Given the comments from companies, FL believes no positive result can be obtained on this topic even when we discuss the discussion in this meeting. Therefore, FL would like to take approach 1 this meeting and to encourages to have offline discussions for the next meeting.
With this analysis, the discussion on this section is closed. If companies have any comments, the following table can be used or further input.
FL has no plan to treat this topic in the online & official offline session during RAN1#112

## Slide 11: L1 measurement: Configurations for L1 measurement - 1
The final FL proposal at RAN1#112 was postponed
[FL proposal 1-7-v3]
For Rel-18 LTM, further study the following structure for L1 measurement configurations.
  Option-1: Based on CSI measurement configuration specified in Rel-17 ICBM
    CSI-MeasConfig for serving cell and candidate cell(s), which requires inter-DU coordination
    For inter-frequency, at least the frequency information, SMTC or measurement gap (MG) with candidate cell are additionally introduced
  Option-2: Introduce an independent a measurement configuration for candidate cell(s) [and serving cell] from serving cell configurations, which, and the measurement configuration is decoupled with serving cell configuration.Introduce an independent measurement configuration for all candidate cell(s) and serving cell(s) (FL note: Suggested by DOCOMO and their intention is to enable reporting for candidate cells with that for serving cell ) from serving cell configurations, which is decoupled with serving cell configuration.
    L1 measurement resource set can be configured outside candidate cell configurations (i.e. ServingCellConfig or CellGroupConfig)
    Separate CSI-MeasCofig is configured for candidate cell from the CSI-MeasConfig for serving cell
  Option-3: Use measurement configuration for each candidate cell
    L1 measurement resource set can be configured inside candidate cell configurations (i.e. ServingCellConfig or CellGroupConfig)
  Option-4: Do not include RS information or cell information in measurement configurations
    For intra-frequency, neither SSB/RS indices nor PCI is configured.
    For inter-frequency, neither SSB/RS indices nor PCI is configured, but frequency information is configured
Note: Proponents of each option are encouraged to bring the detailed explanation in RAN1#112.
Down-selection on the measurement configuration option is expected in RAN1#112
  Option 1 is the most straightforward approach based on Rel-17 LTM
  Option 2 and 3 needs more discussion among companies to avoid the misunderstanding
  Option 4 is a similar concept as L3 mobility (not Rel-17 ICBM). It is simple from network perspective. Meanwhile, it would be complicated from UE perspective.
  FL plan is to spend online/official-offline time for better understanding on each option, and perform the down-selection.
  Clarify the intention of each option as the first step, followed by down-selection between option-1,2,3 vs Option-4 in RAN1#112

## Slide 12: Note: L1 measurement: Configurations for L1 measurement - 1
CSI-ReportConfig ::= SEQUENCE { reportConfigId CSI-ReportConfigId, carrier ServCellIndex OPTIONAL, -- Need S resourcesForChannelMeasurement CSI-ResourceConfigId, csi-IM-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R nzp-CSI-RS-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R reportConfigType CHOICE { :
}, reportQuantity CHOICE { none NULL, cri-RI-PMI-CQI NULL, cri-RI-i1 NULL, cri-RI-i1-CQI SEQUENCE { pdsch-BundleSizeForCSI ENUMERATED {n2, n4} OPTIONAL -- Need S }, cri-RI-CQI NULL, cri-RSRP NULL, ssb-Index-RSRP NULL, cri-RI-LI-PMI-CQI NULL }, : reportQuantity-r16 CHOICE { cri-SINR-r16 NULL, ssb-Index-SINR-r16 NULL } OPTIONAL, -- Need R codebookConfig-r16 CodebookConfig-r16 OPTIONAL -- Need R ]], [[ :
reportQuantity-r17 CHOICE { cri-RSRP-Index-r17 NULL, ssb-Index-RSRP-Index-r17 NULL, cri-SINR-Index-r17 NULL, ssb-Index-SINR-Index-r17 NULL } OPTIONAL -- Need R ]] }
FL’s interpretation of option-1 for L1 measurement configuration
CSI-ReportConfig ::= SEQUENCE { reportConfigId CSI-ReportConfigId, carrier ServCellIndex OPTIONAL, -- Need S resourcesForChannelMeasurement CSI-ResourceConfigId, csi-IM-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R nzp-CSI-RS-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R reportConfigType CHOICE { :
}, reportQuantity CHOICE { none NULL, cri-RI-PMI-CQI NULL, cri-RI-i1 NULL, cri-RI-i1-CQI SEQUENCE { pdsch-BundleSizeForCSI ENUMERATED {n2, n4} OPTIONAL -- Need S }, cri-RI-CQI NULL, cri-RSRP NULL, ssb-Index-RSRP NULL, cri-RI-LI-PMI-CQI NULL }, : reportQuantity-r16 CHOICE { cri-SINR-r16 NULL, ssb-Index-SINR-r16 NULL } OPTIONAL, -- Need R codebookConfig-r16 CodebookConfig-r16 OPTIONAL -- Need R ]], [[ :
reportQuantity-r17 CHOICE { cri-RSRP-Index-r17 NULL, ssb-Index-RSRP-Index-r17 NULL, cri-SINR-Index-r17 NULL, ssb-Index-SINR-Index-r17 NULL } OPTIONAL -- Need R ]] }
MIMOParam-r17 ::= SEQUENCE {
additionalPCI-ToAddModList-r17 SEQUENCE (SIZE(1..maxNrofAdditionalPCI-r17)) OF SSB-MTC-AdditionalPCI-r17 OPTIONAL, -- Need N
additionalPCI-ToReleaseList-r17 SEQUENCE (SIZE(1..maxNrofAdditionalPCI-r17)) OF AdditionalPCIIndex-r17 OPTIONAL, -- Need N
:
}
SSB-MTC-AdditionalPCI-r17 ::= SEQUENCE {
additionalPCIIndex-r17 AdditionalPCIIndex-r17,
additionalPCI-r17 PhysCellId,
}
ServingCellConfig ::= SEQUENCE {
:
csi-MeasConfig SetupRelease { CSI-MeasConfig } OPTIONAL, -- Need M :
mimoParam-r17 SetupRelease {MIMOParam-r17} OPTIONAL, -- Need M
:
}
CSI-MeasConfig ::= SEQUENCE { :
csi-SSB-ResourceSetToAddModList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSet OPTIONAL, -- Need N csi-SSB-ResourceSetToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSetId OPTIONAL, -- Need N csi-ResourceConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfig OPTIONAL, -- Need N csi-ResourceConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfigId OPTIONAL, -- Need N csi-ReportConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfig OPTIONAL, -- Need N csi-ReportConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfigId
: }
CSI-ResourceConfig ::= SEQUENCE { csi-ResourceConfigId CSI-ResourceConfigId, csi-RS-ResourceSetList CHOICE { nzp-CSI-RS-SSB SEQUENCE { nzp-CSI-RS-ResourceSetList SEQUENCE (SIZE (1..maxNrofNZP-CSI-RS-ResourceSetsPerConfig)) OF NZP-CSI-RS-ResourceSetId OPTIONAL, -- Need R csi-SSB-ResourceSetList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSetsPerConfig)) OF CSI-SSB-ResourceSetId OPTIONAL -- Need R }, csi-IM-ResourceSetList SEQUENCE (SIZE (1..maxNrofCSI-IM-ResourceSetsPerConfig)) OF CSI-IM-ResourceSetId }, bwp-Id BWP-Id, resourceType ENUMERATED { aperiodic, semiPersistent, periodic }, ..., [[ csi-SSB-ResourceSetListExt-r17 CSI-SSB-ResourceSetId OPTIONAL -- Need R ]] }
CSI-SSB-ResourceSet ::= SEQUENCE {
csi-SSB-ResourceSetId CSI-SSB-ResourceSetId,
csi-SSB-ResourceList SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF SSB-Index,
...,
[[
servingAdditionalPCIList-r17 SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF ServingAdditionalPCIIndex-r17 OPTIONAL -- Need R
]]
}
ServingAdditionalPCIIndex-r17 ::= INTEGER(0..maxNrofAdditionalPCI-r17)
CSI-SSB-ResourceSet ::= SEQUENCE {
csi-SSB-ResourceSetId CSI-SSB-ResourceSetId,
csi-SSB-ResourceList SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF SSB-Index,
...,
[[
servingAdditionalPCIList-r17 SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF ServingAdditionalPCIIndex-r17 OPTIONAL -- Need R
]]
}
ServingAdditionalPCIIndex-r17 ::= INTEGER(0..maxNrofAdditionalPCI-r17)
Indication of non-serving cell is realized here.
Candidate cell measurement for intra- and inter- frequency is realized by the same approach as ServingAddtinalPCIIndex-r17 e.g. by including frequency information (ARFCN)

## Slide 13: Note: L1 measurement: Configurations for L1 measurement - 1
CSI-ReportConfig ::= SEQUENCE { reportConfigId CSI-ReportConfigId, carrier ServCellIndex OPTIONAL, -- Need S resourcesForChannelMeasurement CSI-ResourceConfigId, csi-IM-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R nzp-CSI-RS-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R reportConfigType CHOICE { :
FL’s interpretation of option-2 for L1 measurement configuration
MIMOParam-r17 ::= SEQUENCE {
additionalPCI-ToAddModList-r17 SEQUENCE (SIZE(1..maxNrofAdditionalPCI-r17)) OF SSB-MTC-AdditionalPCI-r17 OPTIONAL, -- Need N
additionalPCI-ToReleaseList-r17 SEQUENCE (SIZE(1..maxNrofAdditionalPCI-r17)) OF AdditionalPCIIndex-r17 OPTIONAL, -- Need N
:
}
SSB-MTC-AdditionalPCI-r17 ::= SEQUENCE {
additionalPCIIndex-r17 AdditionalPCIIndex-r17,
additionalPCI-r17 PhysCellId,
}
ServingCellConfig ::= SEQUENCE {
:
csi-MeasConfig SetupRelease { CSI-MeasConfig } OPTIONAL, -- Need M :
mimoParam-r17 SetupRelease {MIMOParam-r17} OPTIONAL, -- Need M
:
}
CSI-MeasConfig ::= SEQUENCE { :
csi-SSB-ResourceSetToAddModList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSet OPTIONAL, -- Need N csi-SSB-ResourceSetToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSetId OPTIONAL, -- Need N csi-ResourceConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfig OPTIONAL, -- Need N csi-ResourceConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfigId OPTIONAL, -- Need N csi-ReportConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfig OPTIONAL, -- Need N csi-ReportConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfigId
: }
One or multiple CSI-ReportConfig are intended for intra-frequency reporting, i.e. same as pre-Rel-18 mechanism
CSI-ReportConfig ::= SEQUENCE { reportConfigId CSI-ReportConfigId, carrier ServCellIndex OPTIONAL, -- Need S resourcesForChannelMeasurement CSI-ResourceConfigId, csi-IM-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R nzp-CSI-RS-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R reportConfigType CHOICE { :
Other CSI-ReportConfig are intended for inter-frequency reporting
  Other solution is to define a new IE for inter-freqnecy CSI-Reporting
“carrier” IE is extended (replaced?) to indicate the target frequency
Issue: this approach cannot realize the following agreement at RAN1#111. A solution is needed.
  In a single report instance, report for serving cell and candidate cell(s) for intra-frequency and/or inter-frequency can be included.
Note:
At RAN1#111, this agreement was made without intensive discussion, so it seems companies have different understanding on the interpretation. This is an open issue at RAN1#112

## Slide 14: Note: L1 measurement: Configurations for L1 measurement - 1
CSI-ReportConfig ::= SEQUENCE { reportConfigId CSI-ReportConfigId, carrier ServCellIndex OPTIONAL, -- Need S resourcesForChannelMeasurement CSI-ResourceConfigId, csi-IM-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R nzp-CSI-RS-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R reportConfigType CHOICE { :
FL’s interpretation of option-3 for L1 measurement configuration
ServingCellConfig ::= SEQUENCE {
:
csi-MeasConfig SetupRelease { CSI-MeasConfig } OPTIONAL, -- Need M :
mimoParam-r17 SetupRelease {MIMOParam-r17} OPTIONAL, -- Need M
:
}
CSI-MeasConfig ::= SEQUENCE { :
csi-SSB-ResourceSetToAddModList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSet OPTIONAL, -- Need N csi-SSB-ResourceSetToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSetId OPTIONAL, -- Need N csi-ResourceConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfig OPTIONAL, -- Need N csi-ResourceConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfigId OPTIONAL, -- Need N csi-ReportConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfig OPTIONAL, -- Need N csi-ReportConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfigId
: }
CSI-ReportConfig ::= SEQUENCE { reportConfigId CSI-ReportConfigId, carrier ServCellIndex OPTIONAL, -- Need S resourcesForChannelMeasurement CSI-ResourceConfigId, csi-IM-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R nzp-CSI-RS-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R reportConfigType CHOICE { :
CSI-ReportConfig ::= SEQUENCE { reportConfigId CSI-ReportConfigId, carrier ServCellIndex OPTIONAL, -- Need S resourcesForChannelMeasurement CSI-ResourceConfigId, csi-IM-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R nzp-CSI-RS-ResourcesForInterference CSI-ResourceConfigId OPTIONAL, -- Need R reportConfigType CHOICE { :
ServingCellConfig for serving cell
ServingCellConfig ::= SEQUENCE {
:
csi-MeasConfig SetupRelease { CSI-MeasConfig } OPTIONAL, -- Need M :
mimoParam-r17 SetupRelease {MIMOParam-r17} OPTIONAL, -- Need M
:
}
CSI-MeasConfig ::= SEQUENCE { :
csi-SSB-ResourceSetToAddModList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSet OPTIONAL, -- Need N csi-SSB-ResourceSetToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSets)) OF CSI-SSB-ResourceSetId OPTIONAL, -- Need N csi-ResourceConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfig OPTIONAL, -- Need N csi-ResourceConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ResourceConfigurations)) OF CSI-ResourceConfigId OPTIONAL, -- Need N csi-ReportConfigToAddModList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfig OPTIONAL, -- Need N csi-ReportConfigToReleaseList SEQUENCE (SIZE (1..maxNrofCSI-ReportConfigurations)) OF CSI-ReportConfigId
: }
Issue:
How to define the report configuration (CSI-ReportConfig) for a candidate cell SSB ?
  Is a CSI-ReportConfig in a serving cell ServingCellConig used?
How to refer CSI-ResourceConfig in a ServingCellConfig for a candidate cell?
ServingCellConfig for a candidate cell (delta config) including inter-frequency
14
CSI-ResourceConfig ::= SEQUENCE { csi-ResourceConfigId CSI-ResourceConfigId, csi-RS-ResourceSetList CHOICE { nzp-CSI-RS-SSB SEQUENCE { nzp-CSI-RS-ResourceSetList SEQUENCE (SIZE (1..maxNrofNZP-CSI-RS-ResourceSetsPerConfig)) OF NZP-CSI-RS-ResourceSetId OPTIONAL, -- Need R csi-SSB-ResourceSetList SEQUENCE (SIZE (1..maxNrofCSI-SSB-ResourceSetsPerConfig)) OF CSI-SSB-ResourceSetId OPTIONAL -- Need R :
CSI-SSB-ResourceSet ::= SEQUENCE {
csi-SSB-ResourceSetId CSI-SSB-ResourceSetId,
csi-SSB-ResourceList SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF SSB-Index,
...,
[[
servingAdditionalPCIList-r17 SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF ServingAdditionalPCIIndex-r17 OPTIONAL -- Need R
]]
}
ServingAdditionalPCIIndex-r17 ::= INTEGER(0..maxNrofAdditionalPCI-r17)
CSI-SSB-ResourceSet ::= SEQUENCE {
csi-SSB-ResourceSetId CSI-SSB-ResourceSetId,
csi-SSB-ResourceList SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF SSB-Index,
...,
[[
servingAdditionalPCIList-r17 SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF ServingAdditionalPCIIndex-r17 OPTIONAL -- Need R
]]
}
ServingAdditionalPCIIndex-r17 ::= INTEGER(0..maxNrofAdditionalPCI-r17)
CSI-SSB-ResourceSet ::= SEQUENCE {
csi-SSB-ResourceSetId CSI-SSB-ResourceSetId,
csi-SSB-ResourceList SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF SSB-Index,
...,
[[
servingAdditionalPCIList-r17 SEQUENCE (SIZE(1..maxNrofCSI-SSB-ResourcePerSet)) OF ServingAdditionalPCIIndex-r17 OPTIONAL -- Need R
]]
}
ServingAdditionalPCIIndex-r17 ::= INTEGER(0..maxNrofAdditionalPCI-r17)
refer to serving-cell CSI-SSB-ResourceSet
refer to candidate-cell CSI-SSB-ResourceSet??

## Slide 15: L1 measurement: Configurations for L1 measurement - 2
Agreement
Send an LS to RAN2/RAN3 asking the clarification on intra-/inter-DU scenario:
  RAN1 has started the discussion on the configuration for L1 measurement and TCI states for candidate cells. Regarding the following RAN2 agreements captured in RAN2 LS (R1-2208331/R2-2209257), it is not clear for RAN1 which kind of information/configuration for candidate cell(s) are available at a serving cell for inter-DU case for Rel-18 L1/L2 mobility. Thus, companies have different understanding on the implication of the sentence “as much commonality as reasonable” in the LS.
    The design for intra-DU and inter-DU L1/L2-based mobility should share as much commonality as reasonable. FFS which aspects need to be different.
  RAN1 respectfully asks RAN2 and RAN3 if the serving DU knows the measurement RS configuration and TCI state configuration of cells served by another DU
Reply from RAN2 (R2-2212988) available
  RAN2 assumes that LTM (intra DU and inter DU) is network-controlled mobility where the control is from the source, i.e., measurements (L1 measurements) are configured in the UE from the source Cell, and the decision to switch cell is by the source cell, and enhancements considered for LTM before cell switch, e.g. pre-synchronization, TA handling, target beam management (to the extent it is supported) may be made by the source cell. RAN2 understands that this may require cooperation among source DU, CU, target DU, and/or OAM. RAN2 don’t see any blocking issue to share information between DUs but the support of this is in RAN3 domain. RAN2 see no necessity for a direct inter-DU-interface to support this.
Reply from RAN3 (R3-226829) available
  Regarding Q3 about L1 measurement and TCI state configurations in the LS, RAN3 agreed that based on the current specification, the serving DU cannot know the measurement RS configuration and TCI state configuration of cells served by another DU.
  Any possible consideration for Rel-18 on the coordination over F1 among serving DU, target DU, and CU would need clearly identified requirements from other groups.
RAN1 needs to define a clear requirement to RAN3 to move forward
No immediate RAN1 action is required in RAN1#112

## Slide 16: L1 measurement reporting - 1
More discussion on the report contents would be needed at RAN1#112
  Estimate how many bits are needed for each report instance, which includes number of configured/reported beams/cells, the necessity of grouping etc.
  The container discussion (i.e. whether PUCCH is supported or not) will be put on hold
[Conclusion at RAN1#110b-e]
Agreement (FL proposal 2-1-1)
For L1 measurement report for Rel-18 L1/L2 mobility, further study the following mechanisms:
  Report as UCI on PUCCH or PUSCH
    Periodic report on PUCCH, semi-persistent report on PUCCH/PUSCH, and aperiodic report on PUSCH
    Further study potential enhancements to Rel-17 ICBM report format to accommodate Rel-18 scenarios, e.g.
      Inter-frequency measurement, if supported
      Increasing the maximum number of reported beams, which is 4 for Rel-17 ICBM
      Flexible size beam report, e.g. two-part UCI (e.g., the 1st part contains the best beam/cell and the number (e.g., N) of reported beams/cells, the 2nd part contains the rest (N-1) beams/cells
      Reducing the reporting overhead by e.g. choosing beams/cells per frequency or across frequencies to report (FFS how)
  Report on MAC CE
    Both gNB scheduled and/or UE initiated (if supported) report are studied
[Conclusion at RAN1#111]
Agreement
For gNB scheduled L1 measurement report for Rel-18 LTM, report as UCI is supported
  Semi-persistent report on PUSCH, and aperiodic report on PUSCH are supported
    FFS: periodic and semi-persistent PUCCH
  In a single report instance, report for serving cell and candidate cell(s) for intra-frequency and/or inter-frequency can be included.
FL plan is to spend some time on the technical discussion on report contents (and means to reduce the overhead, if necessary) including solution for inter-freq report in RAN1#112, and make some decisions

## Slide 17: L1 measurement reporting - 2
While the interest level of this UE event triggered report is very high, FL has a strong concern to agree on the introduction without looking at the detailed design.
  The proposals by companies at RAN1#111 have just looked at a focused aspect, no comprehensive analysis was shown
  Different approach can be taken for UE event triggered report. Hence, it would not be easy to come up with a single solution
  FL believes this is an optional feature, i.e. LTM will work without this functionality
If UE event triggered report is specified in Rel-18, FL preference is to simplify the RAN1 discussions e.g. as follows
  Reuse the UE event defined for L3 mobility
  Report container is MAC CE only, i.e. PUSCH is used as a report container
  Further discuss the report format
  UE event triggered report configuration is independent from gNB scheduled reporting
  Report destination is the serving cell only
[Conclusion at RAN1#111]
Agreement
For L1 measurement report for Rel-18 L1/L2 mobility, if UE event triggered report for L1 measurement is supported based on further study
  At least the following aspects may be considered
    How to define UE event and exact definition of events,
    Report container
    Resource allocation/assignment for UE event triggered report
    Necessity of indication to gNB when the condition UE event is met, and how
    Necessity to define the condition to start/stop the reporting,
    Contents of the report/reporting format, PCI, RS ID, measurement result etc.
    The interaction with filtered L1 measurement results (if supported)
    Support of simultaneous configuration of both UE event triggered and any of periodic/semi-persistence/aperiodic reporting, and solutions when both of them are configured.
    Report destination, whether the report is sent to serving cell only or can be sent to one or more candidate cell(s).
    Benefit when L3 measurement is involved
FL plan is to produce a few options (including FL proposal above) for further discussion.
If failed, UE event triggered report will be deprioritized in Rel-18 LTM.

## Slide 18: Beam indication: mechanism
Resolution of FFS (whether/how to design mechanism for Beam indication for Rel-18 LTM when at least one from serving cell and candidate cell supports only Rel-15 TCI framework)
  It would be good (at least from network perspective) to specify a solution for the network which does not support unified TCI framework
    The solution may be simple: “TCI state indication” in LTM trigger MAC CE can just be replaced by “reference QCL-source-RS indication”
    However, the discussion in RAN1 cannot be so simple!: Multiple approach can be considered for configuration, which requires a lot of RAN1 discussions
  The concern to specify both is:
    Standardization work: RAN1 will have no time to define two solutions
    UE complexity: FL wonders if two solution can really be implemented by UE. If so, what is the purpose to specify two solutions in standard??
FL view: Proceed with Rel-17 unified TCI framework at this moment and FFS part can be discussed considering the overall progress
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 3-1)
RAN1 to further study if the beam indication of candidate cell(s) L1/L2 mobility should be designed for a specific TCI framework below, and their potential RAN1 spec impact.
  Option A: Beam indication for Rel-18 L1/L2 mobility is designed based on Rel-17 TCI framework mechanism
  Option B: Beam indication for Rel-18 L1/L2 mobility is designed based on Rel-15 TCI framework mechanism
  Option C: Beam indication for Rel-18 L1/L2 mobility is designed based on both Rel-15 and Rel-17 TCI framework mechanisms
[Conclusion at RAN1#111]
Agreement
The beam indication of candidate cell(s) for Rel-18 LTM should be designed based on the following:
  Beam indication for Rel-18 LTM is designed based on Rel-17 unified TCI framework, if both serving cell and candidate cell support Rel-17 unified TCI framework
  FFS: whether/how to design mechanism for Beam indication for Rel-18 LTM when at least one from serving cell and candidate cell supports only Rel-15 TCI framework.
  Note: How and whether to indicate the new serving cell(s) and timing for beam indication are separately discussed
Check companies’ contribution at RAN1#112, and decide the direction

## Slide 19: Beam indication: Timing of beam indication
With the approval of Scenario 2, FL believes Scenario 1 and 3 are deemed as an optimization
  Scenario 1 can be supported if the UE and gNB supports Rel-17 ICBM
    On top of that, the necessity of specific enhancements needs more discussion
This agreement just give us a high level principle, and we need more detailed discussion on the timing issue
  Indication and activation of TCI state in FFS is a good example
  In addition, update of measurement and report configuration, CSI report, SRS will be an issue
  This may impact on the necessary contents of LTM cell switch command
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 3-2)
From RAN1 perspective, the following scenarios can be considered for Rel-18 L1/L2 mobility for beam indication timing. This will be updated depending on further RAN1 assessment and RAN2 decision on the time chart
  Scenario 1: Beam indication before cell switch command
  Scenario 2: Beam indication together with cell switch command
  Scenario 3: Beam indication after cell switch command
Interested companies are encouraged to further study the validity of the scenarios and the potential spec impact.
[Conclusion at RAN1#111]
Agreement
For beam indication timing for Rel-18 LTM,
  Support Scenario 2: Beam indication together with cell switch command,
    For Rel-17 unified TCI framework,
      Beam indication indicates TCI state for each target serving cell
  FFS: Scenario 1: Beam indication before cell switch command
  FFS: Scenario 3: Beam indication after cell switch command
FFS: Activation of TCI state(s) of target serving and/or candidate cell(s).
RAN1 to check the strong necessity of optimization for scenario 1 and support of scenario 3 from the RAN1#112 contributions. Unless confirmed, these scenarios are deprioritized. (Note: FL believes/assumes scenario 1 (as simultaneous operation of Rel-17 ICBM and Rel-18 LTM) is supported, and it needs to be confirmed/agreed in RAN1#112).
Activation of TCI state(s) for scenarios will be discussed together with other procedure issues.

## Slide 20: Cell switch command
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 4-1)
Interested companies are encouraged to perform technical analysis of the cell switch command from a RAN1 point of view, e.g.
  Necessary information included in the command, which is relevant for RAN1 discussion
  Necessary number of bits for the information
  L1 impact or concern to use DCI or MAC CE for L1/L2 cell switch command
[Conclusion at RAN1#111]
The following proposal was postponed
The following contents are further studied for the contents included in the cell switch command from layer 1 perspective. The bit number required for the contents and the condition of existence needs further discussion.
  Cell identity / Cell group identity – (ID or index?, what is the necessity from physical layer POV)
  TCI state ID/Beam indication –FL note: the relationship with the timing discussion (i.e. beam indication before cell switch command) need to be discussed
  DL/UL BWP indication
  Differentiation between Rel-17 ICBM and Rel-18 LTM (if the DCI for Rel-17 ICBM is reused for cell switch command) FL note: RAN2 agreed to use MAC CE for cell switch triggering on Tuesday in this meeting
  TA value and/or TA acquisition indication
  [UL resource indication for sending acknowledgement of LTM (if RAN1 identify the necessity from L1 point of view) ]
  Triggered aperiodic CSI-RS resource indice(s)/ CSI-RS resource set ID/CSI report setting ID
    e.g. for gNB/UE beam refinement, TRS tracking after cell switch command
  Triggered aperiodic SRS resource set ID
The final form of this proposal is a good starting point of RAN1#112 discussions
Firstly, RAN1 needs to look at the overall procedure for our better understanding
   The same observation as the previous slide

## Slide 21: Preparation for handover before reception of cell switch command
DL synchronization prior to the LTM cell switch command, and RAN1 spec impact would be small
  No immediate action is necessary at RAN1#112
Open issues: RAN1 to discuss whether they are essential or optimization (while FL thinks they are just for optimization: LTM will work without these functionalities)
  TRS tracking for candidate cell(s)
  CSI acquisition for candidate cell(s)
  Activation/Selection of TCI states for candidate cell(s),
[Conclusion at RAN1#110b-e]
Agreement(FL proposal 5-1)
RAN1 to further study the potential RAN1 enhancements and spec impact to perform at least the following procedures prior to the reception of L1/L2 cell switch command aiming at the reduction of handover delay / interruption
  DL synchronization for candidate cell(s)
  TRS tracking for candidate cell(s)
  CSI acquisition for candidate cell(s)
  Activation/Selection of TCI states for candidate cell(s), if feasible FL:Qualcomm suggests to add “activation” back
  Note: Uplink synchronization aspect will not be discussed under this A.I.
FFS: Whether the above procedures prior to the reception of L1/L2 cell switch command can be performed on candidate cell when it is deactivated SCell (if defined in RAN2)
[Conclusion at RAN1#111]
Agreement
Regarding the potential RAN1 enhancements to reduce the handover delay / interruption for Rel-18 LTM
  Support at least DL synchronization for candidate cell(s) based on at least SSB before cell switch command
    Further study the necessary mechanism, e.g. signaling and UE capability
Firstly, RAN1 needs to look at the overall procedure for our better understanding
   The same observation as the previous slide

## Slide 22: Note: Procedure issues (based on scenario 2)
LTM cell switch command
(MAC CE)
HARQ-ACK
Old serving cell
Beam application timing & cell switch completion
New serving cell
(Candidate cell for the old serving cell)
TCI | Cand. cell PCI | Beam index
0 | 3 | 3
1 | 3 | 4
2 | 3 | 5
3 | 3 | 6
TCI | Cand. cell PCI | Beam index
0 | 3 | 3
1 | 3 | 4
2 | 3 | 5
3 | 3 | 6
Question: Is TCI activation procedure necessary given L1(DCI) is not used for beam indication?
Question: Is the definition of beam application timeline necessary?
DL synchronization
[UL synchronization]
(TRS tracking?)
(CSI acquisition?)
Question: Are TRS tracking and CSI acquisition necessary? Essential or optimization?
Candidate information included in cell switch command
TCI state ID/Beam indication
Cell identity / Cell group identity
DL/UL BWP indication
TA value and/or TA acquisition indication  to be confirmed in another AI
Triggered aperiodic CSI-RS resource indice(s)/ CSI-RS resource set ID/CSI report setting ID
Triggered aperiodic SRS resource set ID
Q: immediate CSI reporting on the new serving cell
based on the trigger in the cell switch command?
Q: immediate SRS Tx on the new serving cell
based on the trigger in the cell switch command?
Q: UL and DL BWP is indicated by cell switch command?
RRC configuration (CellGroupConfig) for a candidate cell is activated
Question: How is this list defined/configured? (i.e. definition/configuration of the TCI state pool)
(Measure SSB as QCL type A or C and/or PL RS for activated TCI of candidate cell?)
indication
Activation
TCI pool
(PCI+beam index)
Note: (part of ) the functionality can be decoupled from LTM core functionality (i.e. the usage can be network choice), and UE feature group discussion can be done at the later stage
Notes: Qualcomm 12140: after the MAC-CE command application time, the TCI activation latency also includes the time to measure the 1st transmission of SSB as the QCL-Type A or C source in the TCI state to be activated and corresponding 2 ms processing time

## Slide 23: Note: Procedure issues (based on scenario 1, if introduced)
LTM cell switch command
(MAC CE)
HARQ-ACK
Old serving cell
Beam application timing & cell switch completion
New serving cell
(Candidate cell for the old serving cell)
TCI ID | AdditionalPCI | QCL RS ID
0 | 3 | 3
1 | 3 | 4
2 | 3 | 5
3 | 3 | 6
TCI | Cand. cell PCI | Beam index
0 | 3 | 3
1 | 3 | 4
2 | 3 | 5
3 | 3 | 6
Question: Is the definition of beam application timeline necessary?
DL synchronization
[UL synchronization]
(TRS tracking?)
(CSI acquisition?)
Question: Are TRS tracking and CSI acquisition necessary? Essential or optimization?
Candidate information included in cell switch command
TCI state ID/Beam indication
Cell identity / Cell group identity
DL/UL BWP indication
TA value and/or TA acquisition indication  to be confirmed in another AI
Triggered aperiodic CSI-RS resource indice(s)/ CSI-RS resource set ID/CSI report setting ID
Triggered aperiodic SRS resource set ID
Q: immediate CSI reporting on the new serving cell
based on the trigger in the cell switch command?
Q: immediate SRS Tx on the new serving cell
based on the trigger in the cell switch command?
Q: UL and DL BWP is indicated by cell switch command?
RRC configuration (CellGroupConfig) for a candidate cell is activated
Question:
Is the beam indication by cell switch command necessary for scenario 1?
If yes, the difference between the indication in cell switch command and ?
(Measure SSB as QCL type A or C and/or PL RS for activated TCI of candidate cell?)
indication
Activation
TCI pool
(PCI+beam index)
Activation of TCI states
Question: same as Rel-17 TCI pool (dl-OrJoint-TCIStateList-r17) or some addition necessary?
Early indication
of TCI state
Q: Intra-freq only?
Beam application timing for UE dedicated channels
(same as Rel-17 ICBM?)
switching delay
HARQ-ACK
Note: (part of ) the functionality can be decoupled from LTM core functionality (i.e. the usage can be network choice), and UE feature group discussion can be done at the later stage
Notes: Qualcomm 12140: after the MAC-CE command application time, the TCI activation latency also includes the time to measure the 1st transmission of SSB as the QCL-Type A or C source in the TCI state to be activated and corresponding 2 ms processing time

## Slide 24
Thank you