## Slide 1: Offline report on the handling on PRACH for enhanced coverage mode
Panasonic
3GPP TSG RAN WG1 #75 R1-136057
San Francisco, USA, 11 – 15 November 2013
Agenda item: 6.2.2.2.2

## Slide 2: PRACH starting level in enhanced coverage mode
Methods for PRACH starting level
  Method 1: FFS between Start from lowest leveL or based on defined measurements
  Method 2: Configured by eNB (FFS: dedicated RRC, MAC, and/or (e)PDCCH)
  Method 3: UE remembers the last eNB and the last successful level
Relation with legacy PRACH procedure and enhanced coverage mode PRACH procedure is FFS.
It should be checked following state/procedures covers all PRACH usages.
State | Procedure | Possibility
Attach | - | Method 1 or 3
Idle to connected | - | Method 1 , 2, 3
connected | contention PRACH for SR | Method 1, 2, 3
connected | PDCCH order contention (?) | Method 1, 2, 3
 | PDCCH order non-contention | Method 2
connected | Non-contention PRACH for handover | FFS as the procedure is supported or not