## Slide 1: WF on DRS RSSI and RSRQ
Huawei, HiSilicon, NTT DOCOMO, Sharp, Broadcom, Samsung, Hitachi
R1-142744
3GPP TSG RAN WG1 #77
Seoul, Korea, 19th – 23rd May 2014
Agenda item 6.2.3.2.5

## Slide 2: Proposal
A single RSSI definition is introduced in Rel-12 for DRS-based RSRQ
  Discovery RSSI (DRSSI) is measured on OFDM symbols that cannot contain signals potentially present in a DRS occasion, independently of whether the UE is configured to report CSI-RS-based RRM measurements
  The same DRSSI measurement can be used to derive CRS-based RSRQ and CSI-RS-based RSRQ
RSRQ = N*RSRP/(N*RSRP+DRSSI) for DRS-based measurements
  N is the number of RBs of the DRSSI measurement bandwidth
  The measurements in the numerator and denominator shall be made over the same set of resource blocks.