## Slide 1
6.3.3.2 WF on simulations for enhancement proposals
3GPP TSG RAN WG1 #79 R1-145355
San Francisco, US, 17th – 21st Nov 2014
Nokia Networks, Nokia Corporation

## Slide 2: Proposal -1
  For a given antenna array configuration, an enhancement proposal that requires specifications change should at least be supported with the following:
  A baseline case
    A baseline is considered to have no specification impact to Rel-12 and providing the best performance achievable using Rel-12 specifications
  An enhancement case
    An enhancement is considered to have specification impact to Rel-12
  The enhancement case should at least be evaluated against the baseline case
Antenna array configuration is given by the parameters {M,N,P,Q}
  Baseline and Enhancement cases assume the same values for M, N, P, Q
    1D TXRU virtualization: The total number of associated TXRUs: Q= MTXRU * N * P according to TXRU model-1 (as defined in RAN1#78bis)
    2D TXRU virtualization: The total number of TXRUs Q should be described by the proponent

## Slide 3: Proposal 2
TXRU virtualization models
  For a given array antenna configuration, the Baseline and Enhancement cases can
    assume different virtualization weight vectors ( for1D or 2D virtualization)
    assume different TXRU architecture options (e.g. sub-array architecture, full-connection architecture, 2D architecture)
  Companies are encouraged to additionally provide both baseline and enhancement case results for the same architecture option
  Introduce the following TXRU virtualization model:
    Sub-array partition model 2
    q(i)=w(i)x(i), i=1, .., MTXRU
    The length of w(i) is given by K = M/MTXRU
    w is given by
      a. Option A:
      b. Option B: wk(i) as given by the proponent company
  The description for 2D TXRU virtualization model to be provided by Ericsson on Thursday

## Slide 4: Proposal -3
Companies are encouraged to share details of the baseline case before RAN1#80 via email discussion
  The intention is to allow easy replication of baseline case results
  TXRU virtualization weights (for 1D or 2D virtualization)
  CSI-RS to TXRU virtualization
  CSI-RS port indexing
  Cell association weights and method