## Slide 1: WF on EB/FD-MIMO CSI feedback enhancements
Samsung, ZTE
3GPP TSG RAN WG1 Meeting #80
Athens, Greece, 9th – 13th February 2015
R1-150816

## Slide 2: Background
Purpose of this WF
  Provide a high-level common understanding for further evaluation during this SI on CSI feedback and codebook enhancement schemes, based upon the relevant proposals in the contributions in RAN1#80.

## Slide 3: Proposal
A CSI feedback enhancement scheme for EB/FD-MIMO is defined according to the following:
  The CSI feedback comprises CQI, RI and PMI.
  The PMI corresponds to a composite precoder w for the 3D channel.
    w is a 2NMTXRU ⨉ r matrix, where r is number of layers, i.e., transmission rank, assumed for the precoder w.
    The PMI can be decomposed into multiple smaller information bit fields.
  CQI is derived under the assumption that the UE applies the composite precoder w.
  RI corresponds to r, to be used for the generation of w for CQI calculation.
Other CSI feedback enhancement schemes are not precluded in this SI.

## Slide 4: Proposal
Example rank-1 PMI codebooks (r=1) are defined with the following component precoding vectors:
  wH is a 2N ⨉ 1 azimuth precoding vector
    Ex 1) wH is generated according to the legacy codebook
  v is a MTXRU ⨉ 1 elevation precoding vector
  Ex 1) Kronecker product (KP) codebook:
  Ex 2) Linear-combination of KP precoders:
  Ex 3) Explicit quantization of dominant eigenvector of the channel covariance matrix
  In Ex 1 and 2, subband wH may be selected from a set of candidate beam vectors, just like Rel-10 8-Tx beam selection.

## Slide 5: Proposal
Example options to define the elevation precoding vector v:
  Ex 1) Legacy codebook
    If MTXRU = 2, is a Rel-8 2-Tx codebook
    If MTXRU = 4, is a Rel-8 4-Tx codebook
    If MTXRU = 8, is a Rel-10 8-Tx codebook
  Ex 2) (MTXRU)-Tx DFT codebook with oversampling factor x, where x is a positive integer.

## Slide 6: Proposal
Rank-2 PMI codebook (i.e., with r=2)
  Ex 1) Each column of the precoder is a KP of h and v component precoding vectors
    Ex 1-1) column-wise KP of rank-2 wH and rank-1 v
    Ex 1-2) column-wise KP of rank-1 wH and rank-2 v
Companies are encouraged to bring evaluation results for this CSI feedback proposal and/or other CSI feedback proposals by RAN1#80bis