## Slide 1: WF on PUCCH on SCell for CA
NTT DOCOMO, NEC, Sharp, Softbank Mobile, Intel, Ericsson, KDDI
R1-150823
3GPP TSG RAN WG1 #80
Athens, Greece, 9th – 13th February 2015
Agenda item 7.2.1.1

## Slide 2: Proposal (1)
For Rel.12 CA configurations, set the agreements for PUCCH on SCell achieved during the Rel.12 DC WI as the baseline
  PUCCH transmission on two serving cells is realized by the following methods:
    On the PCell for SCells in PUCCH cell group 1
    On one SCell configured to carry PUCCH for SCells in PUCCH cell group 2
    One SCell can only belong to one PUCCH cell group
    One of the two serving cells is PCell
    No cross-carrier scheduling between cells in different PUCCH cell groups
    PUCCH on SCell can carry HARQ-ACK and CSI
  PUCCH on SCell-only (i.e., no PUCCH on PCell) is not supported in Rel.13

## Slide 3: Proposal (2)
In addition, following details are agreed.
  Common search space is not supported in the SCell carrying PUCCH unless RAN2 identifies its necessity.
  For PUCCH on SCell, the Rel.11 PUCCH power-control is reused.
    RRC parameters for SCell PUCCH PC are independent from those of PCell PUCCH.
    TPC command for PUCCH on SCell is transmitted in DCI(s) on the SCell carrying the PUCCH.
  UE procedure on PUCCH transmission is independent between cell groups.
    DL HARQ-ACK timing
    PUCCH resource determination for HARQ-ACK and/or CSI
    Simultaneous HARQ-ACK + CSI on PUCCH
    Simultaneous HARQ-ACK + SRS in one subframe

## Slide 4: Proposal (3)
Send a LS to RAN2 to inform the RAN1 agreements and to ask concluding following aspects.
  Need/feasibility of scheduling request on SCell carrying PUCCH.
  Need/feasibility of contention-based random access on SCell carrying PUCCH.
  Need/feasibility of supporting activation/de-activation of SCell carrying PUCCH.
  Need/feasibility of supporting common search space on SCell carrying PUCCH.

## Slide 5: Proposal (4)
Continue discussion in RAN1 to resolve following FFS aspects.
  Pathloss estimate for PUCCH carried by an SCell is:
    Alt.1: always based on the RSRP in the SCell carrying the PUCCH
    Alt.2: configurable either based on PCell or based on RSRP in the SCell carrying the PUCCH
    Alt.3: determined by RAN2 – ask RAN2 about the need/feasibility of this configurability
  PHR configuration
    Alt.1: Type 2 PHR for an SCell carrying PUCCH is included in the PHR
    Alt.2: Type 2 PHR for an SCell carrying PUCCH is not included in the PHR
  Application of DCI format 3/3A to the PUCCH on SCell
    Alt.1: TPC command for PUCCH on SCell can be transmitted using DCI format 3/3A in the common search space in the PCell
    Alt.2: DCI format 3/3A is not applicable to PUCCH on SCell