## Slide 1: WF on PBCH RE Mapping in Coverage Enhanced Mode
Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Panasonic, CATT, Huawei, HiSilicon, Samsung, InterDigital, Nokia Networks, Sierra Wireless, Qualcomm, Sony, Intel, LG
R1-150882
3GPP TSG RAN WG1 #80
Athens, Greece, February 9-13, 2015
Agenda item 7.2.1.2.3

## Slide 2: Background
In RAN1#79 we agreed that:
  Agree that “user data and MIB repetition are assumed not to be sent in the same PRBs.”
The available REs in the PRB containing MIB can therefore be utilised for coverage enhancement

## Slide 3: Proposal
For coverage enhancement operation, available REs in PRBs containing MIB are used for PBCH
  Available REs are REs not used for the legacy control region, PSS/SSS and CRS
    Handling of possible collision with CSI-RS in these PRBs is FFS
  The legacy control region is set to 3 OFDM symbols
  NOTE: RE mapping for FDD and TDD are different in at least SF#0
  NOTE: The PBCH repetition may not be an integer