## Slide 1: WF on hidden node problems
Cisco Systems, Broadcom, Ruckus, Sony, CableLabs,…,
R1-153448
3GPP TSG-RAN WG1 Meeting #81
Fukuoka, Japan, 25th-29th May 2015
Document for: Decision
AI 6.2.4.3

## Slide 2: Hidden node problem
Scenario A:
  When a node (node A) is out of transmission range of another node (node B), and the recipient of node B (node B’) is within transmission range of node A, Node A would have no knowledge of the transmission status of node B, and collisions can occur.
Scenario B:
  When node C is within transmission range of both A and B, but A is not within range of B, both A and B may transmit to their respective recipients nodes A’ and B’ at the same time, and thereby blocking transmission opportunities for C.
Node A
Node B
Node B’
Node A
Node B
Node C
Node A’
Node B’
Node C’
Scenario A
Scenario B

## Slide 3: Proposal
Proposal 1:
  RAN1 should capture hidden node aspects in TR 36.889 and further investigate how to handle the issue.
Proposal 2:
  Investigations on hidden node issues may include
    Respecting the NAV (RTS/CTS) from Wi-Fi nodes or
    An alternative mechanism that addresses hidden nodes to the equivalent level that RTS/CTS does for Wi-Fi, and/or
    Increasing CCA sensitivity, i.e. lowering LAA ED threshold