## Slide 1: WF on LAA DL transmission burst(s) configurations
Huawei, HiSilicon, Qualcomm, Samsung, ZTE
3GPP TSG RAN WG1 Meeting #81 R1-153645
Fukuoka, Japan, May 25-29, 2015
Agenda item: 6.2.4.3
Document for decision

## Slide 2: Proposal
Alt1
For each DL transmission burst containing at least PDSCH, the starting position and ending position need to be known to the UE on this carrier
  Determining the start position
    Option1: Blind detect the start position
    Option2: Indicate the start position of the DL transmission burst after the signal to reserve the channel
    Option3: indicate the potential start subframe and blind detect the start position

## Slide 3: Proposal
  Determining the end position
    Option 1: Indicate the end position before the end of DL transmission burst
    Option 2: Indicate the duration of the DL transmission burst
      The duration of the DL transmission burst may be changed and indicated to the UE during this transmission burst
    Option3: No indication of the end position or duration of the DL transmission burst
      The UE assumes the DL transmission burst ends when the maximum transmission duration is achieved for this DL transmission burst
Notes: the duration of any DL transmission burst should be within the maximum transmission duration.

## Slide 4: Proposal
Alt 2
The DL transmission burst containing at least PDSCH is blindly detected by the UE in each subframe on this carrier