## Slide 1: WF on Frequency Hopping
LG Electronics, Qualcomm, InterDigital, Panasonic, Samsung, NEC, Huawei, HiSilicon,
R1-153649
3GPP TSG RAN WG1 #81
Fukuoka, Japan, 25th-29th, May 2015
Agenda item 6.2.1.1

## Slide 2: Proposals on Frequency Hopping
Frequency hopping for MTC SIB-1 is always used at least system bandwidth >= 5Mhz
  The frequency location of MTC SIB-1 is determined based on subframe index (and/or SFN), cell ID and system bandwidth.
For frequency hopping of a channel CH,
  YCH (frequency hopping granularity) is determined based on one of the following options
    Alt 1. A common value is used
      FFS whether YCH is specified in the spec or configured by MIB/SIB1
    Alt 2. Multiple values are used (e.g., a single value per coverage/repetition level)
      FFS the details including mappings
    Alt 3. YCH is variable
      YCH is determined based on repetition number and the number of narrow-bands used for hopping
      One hop per narrowband (one retuning per narrowband)
Note: Hopping pattern of common channels such as SIBx is cell-specific
FFS whether frequency hopping can be used for LC UEs in non-CE
FFS on details of mapping between hopping pattern(s) and channels