## Slide 1: WF on CCA slot and Defer period
Ericsson, Broadcom, [National Instruments],…
3GPP TSG RAN WG1 #82 R1-154790
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Background
Agreement:
If LAA is adopting a LBT category 4 scheme for DL transmission, it will be based on ETSI option B modified to a LBT category 4 scheme except for the following modifications that ensure fairness with Wi-Fi:
  The size of the LAA contention window is variable via dynamic variable backoff or semi-static backoff between X and Y ECCA slots
    One candidate of variable is exponential backoff, FFS for other candidates
    Note that most of evaluations are based on exponential backoff
    The value of X and Y is a configurable parameter
    FFS: which trigger and rate for adapting the size of the contention window
  Consider minimum ECCA slot size smaller than 20 µs
  The initial CCA (ICCA) can be configurable to be comparable to the defer periods of Wi-Fi (e.g., DIFS or AIFS)
    FFS: Conditions under which initial CCA is used
  When ECCA countdown is interrupted, a defer period (not necessarily the same as ICCA) is applied after channel becomes idle
    FFS: Continuing count down during defer period
  The defer period is configurable. It can be configured to be comparable to defer periods of Wi-Fi (e.g. DIFS or AIFS).
    FFS: A defer period configured to be zero.
    FFS: how matching is done when multiple UEs are scheduled in a subframe with different QoS, or when a transmission contains no PDSCH (e.g. DRS, CSI-RS), or when a transmission contains UL grants
  FFS: Relationship, if any, between contention window and maximum channel occupancy?
Discuss the values of all the above parameters at RAN1#81
Defer period: Minimum time that a node has to wait after the channel becomes idle before transmission, i.e., a node can transmit if the channel is sensed to be idle for ≥ defer period.

## Slide 3: Proposal on CCA slot
For LBT Category 4 operation for PDSCH, an ECCA slot size of 9 µs is used for both DL and UL channel access in LAA.
  The actual sensing time is at least 4 µs within the slot.

## Slide 4: Proposal on Defer period
For LBT Category 4 operation for PDSCH
  A defer period consists of a duration of 16 us followed by n consecutive CCA slots.
    n is a positive integer
    The duration of a CCA slot is 9 us.
    FFS on number of slots in the defer period, e.g., n for different QoS classes.
  No count down is performed during the duration of 16 µs at the start of the defer period.
  The backoff counter may be decremented by one at the end of a defer period when all the n slot are observed to be idle.
    If the counter reaches 0 after decrementing, the node shall not transmit immediately and continues the ECCA procedure by performing a CCA check for at least one slot
  The defer period may be aborted when any of the CCA slots is observed to be busy