## Slide 1: WF on Description of Symbol Level Superposition of MUST
ZTE, LGE
3GPP TSG RAN WG1 #82 R1-154847
Beijing, China, 24 – 28 August 2015
Agenda Item: 7.2.7.1

## Slide 2: Proposal
To adopt the high level description on the next page as the base for the text proposal of symbol level superposition schemes for MUST

## Slide 3
“n” number of coded bits of far UE and “m” number of coded bits of near UE come into bit concatenation to form a “(m+n)” bit long concatenated sequence [a1, …, an, b1, …, bm]
The sequence [a1, …, an, b1, …, bm] undergoes constellation mapping to form “n” number of bits [c1, …, cn] and “m” number of bits [d1, …, dm], where the actual mapping may depend on the power partition:
  Direct superposition: [c1, …, cn] = [a1, …, an ] , and [d1, …, dm] = [b1, …, bm]. Gray mapping not guaranteed
  General mapping : [c1, …, cn, d1, …, dm] = p([a1, …, an, b1, …, bm ] ), where p(.) defines certain binary operation. Gray mapping is the primary target
Bit sequence [c1, …, cn] is modulated by Rel-12 QPSK or 2n -QAM modulation
Bit sequence [d1, …, dm] is modulated by Rel-12 QPSK or 2m -QAM modulation
2n –QPSK/QAM symbol and 2m –QPSK/QAM symbol are linearly superposed with weight sqrt(P2) and sqrt(P1), respectively, to form a combined modulation symbol which is generally non-uniform.
Coded bits of far UE
Bit concatenation
2n-PSK/QAM Modulation
2m-PSK/QAM Modulation
Power partition
Combined
superposition
symbols
Coded bits of near UE
a1,…,an
b1,…,bm
Constellation mapping
a1,…,bm
c1,…,cn
d1,…,dm
Bit swapping
f(.)