## Slide 1: WF on LAA Energy Detection Threshold
Cisco Systems, Broadcom
3GPP TSG RAN WG1 #82 R1-154907
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Motivation
In an all Wi-Fi network, nodes perform preamble detection <= -82 dBm.
In a co-existence scenario where signals from LAA arrive at Wi-Fi below -62 dBm,
  If LAA can sense the presence of Wi-Fi and vice-versa, best performance is achieved [R1-152937]
  Else, both Wi-Fi and LAA do not back off to each other.
    More simultaneous LAA transmissions create increased interference at the Wi-Fi network.

## Slide 3: Motivation (Contd.)
Transparent LAA operation is important
  to preclude LAA behavior in which it does not back-off to Wi-Fi even after detecting their presence.
  ensure that future cross-technology RAT can adapt to LAA behavior

## Slide 4: Proposal on Thresholds for LAA Downlink
  For DL channel access for an LAA Scell, LAA shall adopt an adaptable energy detection threshold, chosen within the set {X, Y}, Y < X.
  Alt1: X = A + (23 – Ph) + 10log(W) dBm,
    A = -75 dBm/MHz
    Ph is the maximum eNB transmission power within unlicensed.
    W is the Scell BW (in MHz)
  Alt2: X = A for Ph <= 23 dBm and X = A + (23 – Ph) otherwise.
  FFS: A > -75 dBm/MHz
  FFS: Y
Adaptation rules should be identified in RAN1 .