## Slide 1: WF on SRS support for MTC
Ericsson, Qualcomm, Sequans, Verizon, Panasonic, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell
R1-156176
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th - 9th October 2015
Agenda item 7.2.1.9

## Slide 2: Proposal
LC/CE UE does not support SRS transmission
The following fields in cell-specific SRS configuration are broadcast to LC/CE UE:
  srs-BandwidthConfig
  srs-SubframeConfig
  ackNackSRS-SimultaneousTransmission
If subframe n is not part of UL repetitions, the UE punctures last SC-FDMA symbol in UL transmission in subframe n as required by cell-specific SRS pattern, and ‘puncture’ means Rel-12 behavior
FFS: If subframe n is part of UL repetitions