## Slide 1: WF on PUSCH / PUCCH collision handling
Qualcomm, Sony, Intel, Samsung, Lenovo, InterDigital, Ericsson, Huawei, HiSi
R1-156237
3GPP TSG RAN WG1 Meeting #82bis
Malmo, Sweden, 5th - 9th August 2015
Agenda item 7.2.1.5

## Slide 2: Background
Current agreements in timing:
  PDSCHPUCCH
    In FDD and HD-FDD, if PDSCH transmission ends in subframe n as indicated by the corresponding M-PDCCH, PUCCH carrying HARQ-ACK starts in subframe n+k
  MPDCCHPUSCH
    In FDD and HD-FDD, the PUSCH starts in subframe n+k, where n is the subframe where the repetitions of the decoded M-PDCCH message(s) ends
There is a possible collision (partial or total) between PUSCH and PUCCH for UE in coverage enhancement

## Slide 3: Proposal
MTC UE does not support non-contiguous UL resource allocations within a component carrier
  nonContiguousUL-RA-WithinCC-Info-r10 is always set to NOT supported
Simultaneous PUCCH and PUSCH is not supported
For the subframes where PUSCH repetition and PUCCH repetition overlaps,
  If full overlap:
    Option 1: ACK is multiplexed with PUSCH
    Option 2: Drop PUSCH
  If partial overlap:
    Option 1: Drop PUSCH during overlap portion
    Option 2: Drop the later channel
    Option 3: ACK is multiplexed with PUSCH on overlapped subframes