## Slide 1: Way Forward on 256QAM study for UE category 10 and below
Intel Corporation, AT&T, China Telecom, China Unicom, CMCC, Deutsche Telekom, DISH Network, KT Corporation, SK Telecom, Telstra, Verizon Wireless, Vodafone
AGENDA: 7.1
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th - 9th October 2015
R1-156339

## Slide 2: Proposal
Send an LS to RAN and RAN2 summarizing the RAN1 study on 256QAM support in the UE categories 10 and below for their decision in RAN#70, as shown in Slide 3.

## Slide 3: LS content
To RAN and RAN2 with following observations:
  To support 256QAM for UE category 10 and below in Rel-12 and onwards, RAN1 sees no RAN1 specification impact (other than RAN2 specification impact on TS36.306) with the following notes:
    256QAM for the UE categories 10 and below can be supported by keeping “Maximum number of DL-SCH transport block bits received within a TTI” and “Total number of soft channel bits” in the downlink physical layer parameter values of UE categories defined by TS 36.306
    The “Maximum number of bits of a DL-SCH transport block received within a TTI” the downlink physical layer parameter values of UE categories defined by TS 36.306 should be increased to support 256QAM in the UE categories 10 and below
    The example of the downlink physical layer parameter values of UE categories 6,7,9,10 defined by TS 36.306 is provided in the table
    RAN1 study showed that the support of 256QAM for the UE categories 10 and below is beneficial
UE Category | Maximum number of DL-SCH transport block bits received within a TTI (Note) | Maximum number of bits of a DL-SCH transport block received within a TTI | Total number of soft channel bits | Maximum number of supported layers for spatial multiplexing in DL
… | … | … | … | …
DL Category 6 | 301504 | 149776 (4 layers, 64QAM) 195816 (4 layers, 256QAM) 75376 (2 layers, 64QAM) 97896 (2 layers, 256QAM) | 3654144 | 2 or 4
DL Category 7 | 301504 | 149776 (4 layers, 64QAM) 195816 (4 layers, 256QAM) 75376 (2 layers, 64QAM) 97896 (2 layers, 256QAM) | 3654144 | 2 or 4
DL Category 9 | 452256 | 149776 (4 layers, 64QAM) 195816 (4 layers, 256QAM) 75376 (2 layers, 64QAM) 97896 (2 layers, 256QAM) | 5481216 | 2 or 4
DL Category 10 | 452256 | 149776 (4 layers, 64QAM) 195816 (4 layers, 256QAM) 75376 (2 layers, 64QAM) 97896 (2 layers, 256QAM) | 5481216 | 2 or 4
… | … | … | … | …