## Slide 1
Source: Samsung
LLS results on CSI-RS transmission
with CDM-2 and CDM-4
Agenda Item: 7.2.4.2.1, Document for: Discussion and Decision
R1-156346
3GPP TSG RAN WG1 #82bis
Malmö, Sweden, 5th – 9th October 2015

## Slide 2: Evaluated 16 TX CSI-RS Mapping Patterns
CDM4 pattern
CDM2 pattern
Frequency |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | 15/16 |  |  | 
 |  |  |  |  |  |  |  |  |  | 19/20 |  |  | 
 |  |  |  |  |  |  |  |  |  | 23/24 |  |  | 
 |  |  |  |  |  |  |  |  |  | 27/28 |  |  | 
 |  |  |  |  |  |  |  |  |  | 17/18 |  |  | 
 |  |  |  |  |  |  |  |  |  | 21/22 |  |  | 
 |  |  |  |  |  |  |  |  |  | 25/26 |  |  | 
 |  |  |  |  |  |  |  |  |  | 29/30 |  |  | 
 | Slot 0 |  |  |  |  |  |  | Slot 1 |  |  |  |  | 
Frequency |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | 15/16/ 17/18 |  |  | 
 |  |  |  |  |  |  |  |  |  | 19/20/ 21/22 |  |  | 
 |  |  |  |  |  |  |  |  |  | 23/24/ 25/26 |  |  | 
 |  |  |  |  |  |  |  |  |  | 27/28/ 29/30 |  |  | 
 |  |  |  |  |  |  |  |  |  | 15/16/ 17/18 |  |  | 
 |  |  |  |  |  |  |  |  |  | 19/20/ 21/22 |  |  | 
 |  |  |  |  |  |  |  |  |  | 23/24/ 25/26 |  |  | 
 |  |  |  |  |  |  |  |  |  | 27/28/ 29/30 |  |  | 
 | Slot 0 |  |  |  |  |  |  | Slot 1 |  |  |  |  | 

## Slide 3: Simulation
Evaluation assumptions
Parameters (common) | Value / Comment
Transmission bandwidth | 5MHz
Channel model, UE velocity, spatial correlation | 3GPP ETU channel without correlation, 15 and 30 km/h
Antenna configuration | 16Tx / 2 Rx antennas
Detector | MMSE receiver
PDCCH / PDSCH configuration | 2 / 12 OFDM symbols per sub-frame
Modulation, code rates | Specification CQI based link adaptation
HARQ | Synchronous HARQ with Chase Combining (max 4 transmissions)
Number of allocated PRBs | 4 PRBs scheduled
CSI feedback | CQI/PMI/RI Mode 1-1 based on 16Tx codebook (rank1/2)
Feedback delay | 2 msec
Feedback periodicity | 5 msec
Channel estimation for demodulation | 2D MMSE
Channel estimation for CQI/PMI/RI computation | 1D MMSE
Rank adaptation | On

## Slide 4: Simulation
LLS evaluation results (ETU channel)
UE mobility | CSI-RS | Avg. throughput [bps/Hz] |  |  |  |  |  |  |  | 
 |  | SNR (-3dB) | SNR (0dB) | SNR (3dB) | SNR (6dB) | SNR (9dB) | SNR (12dB) | SNR (15dB) | SNR (18dB) | SNR (21dB)
15 km/h | CDM4 6dB boosting | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100%
 | CDM2 6dB boosting | 100% | 85% | 92% | 95% | 96% | 99% | 100% | 100% | 100%
UE mobility | CSI-RS | Avg. throughput [bps/Hz] |  |  |  |  |  |  |  | 
 |  | SNR (-3dB) | SNR (0dB) | SNR (3dB) | SNR (6dB) | SNR (9dB) | SNR (12dB) | SNR (15dB) | SNR (18dB) | SNR (21dB)
30 km/h | CDM4 6dB boosting | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100% | 100%
 | CDM2 6dB boosting | 100% | 97% | 97% | 99% | 101% | 101% | 100% | 100% | 100%

## Slide 5: Appendix

## Slide 6: Multi-path fading channel
Multi-path fading propagation conditions [TS36.101]
  Delay profiles
Model | Number of channel taps | Delay spread (r.m.s.) | Maximum excess tap delay (span) | 
Extended Pedestrian A (EPA) | 7 | 45 ns | 410 ns | 444KHz
Extended Vehicular A model (EVA) | 9 | 357 ns | 2510 ns | 56KHz
Extended Typical Urban model (ETU) | 9 | 991 ns | 5000 ns | 20KHz
Table B.2.1-1 Delay profiles for E-UTRA channel models
Excess tap delay [ns] | Relative power [dB]
0 | 0.0
30 | -1.0
70 | -2.0
90 | -3.0
110 | -8.0
190 | -17.2
410 | -20.8
Table B.2.1-2 Extended Pedestrian A model (EPA)
Excess tap delay [ns] | Relative power [dB]
0 | 0.0
30 | -1.5
150 | -1.4
310 | -3.6
370 | -0.6
710 | -9.1
1090 | -7.0
1730 | -12.0
2510 | -16.9
Table B.2.1-3 Extended Vehicular A model (EVA)
Excess tap delay [ns] | Relative power [dB]
0 | -1.0
50 | -1.0
120 | -1.0
200 | 0.0
230 | 0.0
500 | 0.0
1600 | -3.0
2300 | -5.0
5000 | -7.0
Table B.2.1-4 Extended Typical Urban model (ETU)