## Slide 1: WF on aperiodic CSI feedback
NEC, NTT DOCOMO, Intel, LG Electronics, Qualcomm
R1-156229
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.2.1.3

## Slide 2: Proposal 1
For existing aperiodic CSI reporting modes/mechanisms,
  One CSI triggering DCI is able to trigger report for at most 32 CSI processes
  i.e., each CSI set can contain at most 32 CSI processes
    Note that the maximum number of CSI processes for each CSI set depends on UE capability
    Introduce new UE capability signaling which indicates the maximum number of CSI processes per UE across CCs per CSI set
  If the number of CSI process is more than 8 and exceeds UE capability, some relaxations to address UE complexity should be considered

## Slide 3: Proposal 2
For A-CSI reporting without UL-SCH,
  No restriction on the maximum number of PUSCH PRBs when A-CSI reporting is triggered by the 3-bit A-CSI request field.