## Slide 1: WF on O1, O2 combinations
CATT, Ericsson, Samsung
3GPP TSG-RAN1#82bis,
Malmo, Sweden, Oct. 5 – 9, 2015
R1-156296

## Slide 2: Background
Rel.13 class A codebook configured with 5 RRC parameters:
  N1, N2= {1,2,3,4,8} where the valid candidates are (N1, N2) = (8,1), (2,2), (2,3), (3,2), (2,4), (4,2)
  O1, O2= {2,4,8}
    For each (N1, N2), configurability of (O1, O2) is restricted to two possible fixed pairs
    Exact values TBD by Fri, 10/09/2015
  Config = {1, 2, 3, 4}
  Note: For dimension with one port, oversampling factor and Config = {2, 3} do not apply
Given the set of values of N1,N2,O1,O2:
  W1 matrices with (L'1,L'2) = (4,2), (2,4) are constructed for N1>=N2and N1<N2, respectively
  where is the index for
  An associated codebook table is defined in terms of i'2, i11 and i12 (refer to slide 5)
Given the value of Config, a subset of codewords from the codebook table is selected as an active subset of values of i'2, associated with one of the following 4 configurations: (see slide 5)
  Config=1: (L1,L2) = (1,1) for rank 1-2
  Config =2: (L1,L2) = (2,2) for rank 1-2 [square]
  Config =3: (L1,L2) = (2,2) for rank 1-2 [non-adjacent 2D beams/checkerboard]
  Config=4: (L1,L2) = (4,1), (1,4) for N1>=N2and N1<N2respectively for rank 1-2
  TBD rank 3-8

## Slide 3: Proposal
(N1,N2) | (O1,O2) combinations
(8,1) | (4,-), (8,-)
(2,2) | (4,4), (8,8)
(2,3) | (8,4), (8,8)
(3,2) | (8,4), (4,4)
(2,4) | (8,4), (8,8)
(4,2) | (8,4), (4,4)
Following table with (O1,O2) combinations for each (N1, N2)
Notes: um