## Slide 1: Proposals on potential power-control parameters for new PUCCH format(s)
NTT DOCOMO, INC.
R1-156311
3GPP TSG RAN WG1 #82bis
Malmo, Sweden, 5th – 9th October 2015
Agenda item 7.2.2.1.1

## Slide 2: Proposals (1)
For the PUSCH-like new PUCCH format, one of following power control formula is applied.
  Option 1: Re-use of existing PUSCH power-control formula with the following exceptions:
    MPUSCH,c(i) is replaced by the number of PRBs of the PUSCH-like PUCCH format.
    Po_PUSCH,c(j) is replaced by the new RRC parameter for the PUSCH-like PUCCH format.
    ac(j) is not configurable and fixed to 1.
    fc(i) is replaced by gc(i), which is the current PUCCH power control adjustment state.
    FFS: whether/how to determine the parameter DTF,c(i).

## Slide 3: Proposals (2)
For the PUSCH-like new PUCCH format, one of following power control formula is applied.
  Option 2: Re-use of existing PUCCH power-control formula with the following exceptions:
    A term 10log10(MPUCCH,c(i)) is included (Note: this was already agreed).
    FFS: how/whether to determine h-function.

## Slide 4: Proposals (3)
For the other new PUCCH format with CDM (if supported),
  If the other new PUCCH format with CDM is the spreading within SC-FDMA symbols, the power-control formula of the PUSCH-like new PUCCH format is re-used with the following exception:
    FFS: different values for power-offset, e.g., DTF,c(i) or DF_PUCCH(F).
  If the other new PUCCH format with CDM is the multi-PRB PUCCH format 3, the power-control formula of the PUCCH format 3 is re-used with the following exception:
    A term 10log10(MPUCCH,c(i)) is included.