## Slide 1: Virtual Cell ID for SRS
Ericsson
Agenda Item: 6.2.4.2.2
Document for: Discussion and Decision
3GPP TSG-RAN WG1#83 R1-157530
Anaheim, US, 16th - 20th November 2015

## Slide 2: Background
Current Rel.13 SRS enhancements are targeting small cells with little attention to FDD
  Extended SRS in UpPTS -> Reduced guard period
  Increased RPF and CS -> smaller delay spread
SRS enhancement for macro cells needed in Rel-13
  To increase capacity and reduce interference (large cells tend to cover many UEs so capacity even more important than for small cells)
  For TDD as well as for FDD

## Slide 3: Background
Macro node
CELL ID 1
CELL ID 2
CELL ID 3
(V/H/2D) Sectorisation (Category 1 enhancement in TR 36.897) based on separate cells
  Problems with mobility if CRS are overlapping
  Problems with CQI estimation with colliding CRS
  Problems with CRS to PDSCH interference if CRS are frequency-shifted
Solution -> Introduce shared cell by beamforming (Category 2 enhancement in TR 36.897)
  Same CRS in all sectors
    CSI measurements measure actual traffic load
    Solves mobility issue when moving across sectors
    Lower CRS to PDSCH interference (no-intra point interference)

## Slide 4: Background
So shared cell by beamforming (Cat.2) solves important problems in downlink
Different sectors may have different Virtual Cell ID for PUCCH,PUSCH and PDSCH DMRS, CSI-RS
  DCI format 2C, 2D can select from two VCID for PDSCH DMRS
  Reduces DMRS interference across sectors
Issue: But use of Cat.2 means different sectors have same Cell ID (→ same scrambling sequence) for SRS!
  Problems with SRS capacity since RPF=2, CS=8 is limiting (small cell enhancements not applicable due to larger cells)
  Problems with SRS interference in case spatial re-use of SRS is introduced in an attempt to increase SRS capacity
Solution -> Introduce Virtual Cell ID for SRS
  Increases SRS capacity
  Reduces SRS interference (to same level as if separate cells would have been used)
Virtual cell ID for SRS allows virtual sectorization to solve CRS and handover problems in DL while avoiding SRS capacity/interference problems in UL!

## Slide 5: Proposal
Introduce VCID for SRS in Rel.13
  The same VCID as used for PUCCH DMRS is used for SRS VCID
    Thus no RRC spec impact
  Hence, VCID for PUCCH and SRS is enabled simultaneously