## Slide 1: WF on FD-MIMO CSI-RS
Samsung, Ericsson, NTT DOCOMO, Intel, AT&T, CHTTL, Fraunhofer HHI, ITRI, Qualcomm, Nokia Networks, ITL, ALU, ASB, Panasonic, Fujitsu, LGE, DT, China Telecom
R1-177710
Agenda Item: 6.2.4.2.1
Document for: Discussion and Decision
3GPP TSG-RAN WG1#83
Anaheim, US, 16th - 20th November 2015

## Slide 2: Background
(1) CDM-2 two-port aggregation and (2) CDM-4 are beneficial respectively for flexible CSI-RS mapping and full-power utilization.
No fundamental problems are identified for proposals (1) and (2).
  Rate of residual phase offset change over time is relatively slow, and residual phase offset can be compensated by UE implementation.
  (1) provides additional flexibility for the network deployment, and no additional UE complexity is anticipated.
  (2) provides performance/MSE gain at low SNR regime and for cell-edge UEs, according to R1-156783, R1-157052 and R1-157204

## Slide 3: Proposal
All the working assumptions on FD-MIMO CSI-RS in RAN1#82b are confirmed.

## Slide 4: Proposals
CDM-4 OCC applies in the following 4 REs comprising a CDM group according to the following table
OCC index | OCC on REs [a b c d]
0 | [1 1 1 1]
1 | [1 -1 1 -1]
2 | [1 1 -1 -1]
3 | [1 -1 -1 1]

## Slide 5: Proposals
16-port CSI-RS RE mapping details for CDM-4
  (N,K) = (8,2)
  8 REs used for mapping legacy 8-port CSI-RS are partitioned into two groups of 4 REs, and each group of 4 REs comprises a CDM group.
  Antenna port numbering and OCC allocation is according to the following table:
CSI-RS ports for a CDM-4 set | OCC indices | RE locations
15,16,19,20 | 0, 1, 2, 3 | RE locations for ports {15,16,19,20} for the first 8-port resource
17,18,21,22 | 0, 1, 2, 3 | RE locations for antenna ports {17,18,21,22} for the first 8-port resource
23,24,27,28 | 0, 1, 2, 3 | RE locations for antenna ports {15,16,19,20} for the second 8-port resource
25,26,29,30 | 0, 1, 2, 3 | RE locations for antenna ports {17,18,21,22} for the second 8-port resource
Illustration: For information

## Slide 6: Proposals
12-port CSI-RS RE mapping details for CDM-4
  (N,K) = (4,3)
  4 REs used for mapping legacy 4-port CSI-RS comprise a CDM group.
  Antenna port numbering and OCC allocation is according to the following table:
CSI-RS ports for a CDM-4 set | OCC indices | RE locations
15,16,17,18 | 0, 1, 2, 3 | 4 REs corresponding to the 1st resource
19,20,21,22 | 0, 1, 2, 3 | 4 REs corresponding to the 2nd resource
23,24,25,26 | 0, 1, 2, 3 | 4 REs corresponding to the 3rd resource
27,28,29,30 | 0, 1, 2, 3 | 4 REs corresponding to the 1st resource
Illustration: For information

## Slide 7: Appendix: RAN1#82b agreements/working assumption