## Slide 1: WF on NB-PRACH power ramping
ZTE, Ericsson …
R1-163445
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th - 15th April 2016
Agenda item 7.2.1.2.4

## Slide 2: Background
For NB-IoT
  If more than one repetition level is configured in the cell, then the UE transmits NB-PRACH with max power except for the lowest repetition level
  Otherwise, the UE uses NB-PRACH power ramping
NB-PRACH resource bandwidth is 3.75 kHz, but PRACH resource bandwidth in LTE system is 6 PRB (1.08 MHz)
Only two preamble formats with different CP lengths are provided in NB-IoT to support different cell sizes

## Slide 3: Proposal
Reuse the following power ramping for NB-PRACH
  Set PREAMBLE_RECEIVED_TARGET_POWER to preambleInitialReceivedTargetPower + DELTA_PREAMBLE + (PREAMBLE_TRANSMISSION_COUNTER – 1) * powerRampingStep
    Reduce the value range of preambleInitialReceivedTargetPower
      FFS the value reduced: [20] or [24] dB
      Note 1: the value reduced 20 dB means that the value range is {-140, -138, -136, -134, -132, -130, -128, -126, -124, -122, -120, -118, -116, -114, -112, -110} dBm
      Note 2: the value reduced 24 dB means that the value range is {-144, -142, -140, -138, -136, -134, -132, -130, -128, -126, -124, -122, -120, -118, -116, -114} dBm
    DELTA_PREAMBLE is set to 0
    Value range of powerRampingStep is the same as LTE: {0, 2, 4, 6} dB