## Slide 1: WF on LOS pathloss model
Huawei, HiSilicon
R1-163483
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th - 15th April 2016
Agenda Item: 8.2.1

## Slide 2: Background
The working assumption for LOS pathloss has discontinuity issue across the break point distance.
Try to resolve the problem, amendment is proposed.

## Slide 3: Proposal
The below pathloss models for LOS are agreed
  The applicable frequency range of the PL formula is fL < fc < 100 GHz, where fL = 0.8 GHz.
* As defined in 36.873, d‘BP = 4 h’BS h‘UT fc/c, where fc is the centre frequency in Hz, c = 3.0108 m/s is the propagation velocity in free space, and h’BS and h‘UT are the effective antenna heights at the BS and the UT, respectively. In UMi scenario the effective antenna heights h’BS and h‘UT are computed as follows: h’BS = hBS – 1.0 m, h‘UT = hUT–1.0 m, where hBS and hUT are the actual antenna heights, and the effective environment height is assumed to be equal to 1.0 m. In UMa scenario the effective antenna heights h’BS and h‘UT are computed as follows: h’BS = hBS – hE, h‘UT = hUT – hE, where hBS and hUT are the actual antenna heights, and the effective environment height hE is a function of the link between a BS and a UT. In the event that the link is determined to be LOS, hE=1m with a probability equal to 1/(1+C(d2D, hUT)) and chosen from a discrete uniform distribution uniform(12,15,…,(hUT-1.5)) otherwise.