## Slide 1: WF on link level channel models for LOS
Huawei, HiSilicon, Spirent, NTT DOCOMO, Vodafone, CMCC, CATT, CATR
R1-163489
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th - 15th April 2016
Agenda Item: 8.2.5

## Slide 2: Background
The link level models agree in Ljubljana meeting included NLOS cases only.
During the email discussion on link level channel model, it was proposed to include LOS models as well (Item #3, ”Companies are encouraged to propose CDL and TDL models for LOS scenario.” from the summary of email discussion)
From the link level modelling point of view, the main difference between the NLOS and LOS models is K factor. The first cluster will have non-fading LOS peak which is modelled as Rice fading in the TDL model.

## Slide 3: Proposal
Proposal 1: Link level channel models for the LOS case are included in the TR.
Proposal 2: The LOS channel models are generated by the same method as the NLOS channel models were already generated.
Proposal 3: The LOS channel model tables in following pages are adopted as way forward.
Note: The CDL models for LOS are created by the same way as the NLOS models: using the 3GPP-3D/WINNER+ parameterization and creating one drop by using the Anite/Keysight GCM Tool. The CDL-D is based on InH and CDL-E is based on UMa, both with elevation parameters based on WINNER+/3GPP-3D.

## Slide 4: CDL-D
Clusters |  |  |  |  |  |  |  |  | 
Cluster | Cluster | Delay | Power | AoD |  | AoA | ZoD |  | ZoA
# | PAS | s | dB | º |  | º | º |  | º
1 | Specular (LOS path) | 0 | -0.2 | 0 |  | -180 | 98.5 |  | 81.5
 | Laplacian | 0 | -13.5 | 0 |  | -180 | 98.5 |  | 81.5
2 | Laplacian | 0.035 | -18.8 | 89.2 |  | 89.2 | 85.5 |  | 86.9
3 | Laplacian | 0.612 | -21 | 89.2 |  | 89.2 | 85.5 |  | 86.9
4 | Laplacian | 1.363 | -22.8 | 89.2 |  | 89.2 | 85.5 |  | 86.9
5 | Laplacian | 1.405 | -17.9 | 13 |  | 163 | 97.5 |  | 79.4
6 | Laplacian | 1.804 | -20.1 | 13 |  | 163 | 97.5 |  | 79.4
7 | Laplacian | 2.596 | -21.9 | 13 |  | 163 | 97.5 |  | 79.4
8 | Laplacian | 1.775 | -22.9 | 34.6 |  | -137 | 98.5 |  | 78.2
9 | Laplacian | 4.042 | -27.8 | -64.5 |  | 74.5 | 88.4 |  | 73.6
10 | Laplacian | 7.937 | -23.6 | -32.9 |  | 127.7 | 91.3 |  | 78.3
11 | Laplacian | 9.424 | -24.8 | 52.6 |  | -119.6 | 103.8 |  | 87
12 | Laplacian | 9.708 | -30.0 | -132.1 |  | -9.1 | 80.3 |  | 70.6
13 | Laplacian | 12.525 | -27.7 | 77.2 |  | -83.8 | 86.5 |  | 72.9
Per-Cluster Parameters |  |  |  |  |  |  |  |  | 
Parameter |  | ASD | ASA | ZSD | ZSA |  |  | XPR | 
Unit |  | º | º | º | º |  |  | dB | 
Value |  | 5 | 8 | 3 | 3 |  |  | 11 | 

## Slide 5: TDL-D
Tap | Delay | Power | Fading distribution
# | ns | dB | 
1 | 0 | 0 | Rice, K = 13.3 dB
2 | 0.035 | -18.8 | Rayleigh
3 | 0.612 | -21 | Rayleigh
4 | 1.363 | -22.8 | Rayleigh
5 | 1.405 | -17.9 | Rayleigh
6 | 1.804 | -20.1 | Rayleigh
7 | 2.596 | -21.9 | Rayleigh
8 | 1.775 | -22.9 | Rayleigh
9 | 4.042 | -27.8 | Rayleigh
10 | 7.937 | -23.6 | Rayleigh
11 | 9.424 | -24.8 | Rayleigh
12 | 9.708 | -30.0 | Rayleigh
13 | 12.525 | -27.7 | Rayleigh

## Slide 6: CDL-E
 |  | Clusters |  |  |  |  |  |  |  |  | 
Cluster | Cluster |  | Delay |  | Power | AoD |  | AoA | ZoD |  | ZoA
# | PAS |  | s |  | dB | º |  | º | º |  | º
1 | Specular (LOS path) |  | 0.000 |  | -0.03 | 0 |  | -180 | 99.6 |  | 80.4
 | Laplacian |  | 0.000 |  | -22.03 | 0 |  | -180 | 99.6 |  | 80.4
2 | Laplacian |  | 0.485 |  | -15.8 | 57.5 |  | 18.2 | 104.2 |  | 80.4
3 | Laplacian |  | 0.514 |  | -18.1 | 57.5 |  | 18.2 | 104.2 |  | 80.4
4 | Laplacian |  | 0.532 |  | -19.8 | 57.5 |  | 18.2 | 104.2 |  | 80.4
5 | Laplacian |  | 0.514 |  | -22.9 | -20.1 |  | 101.8 | 99.4 |  | 80.8
6 | Laplacian |  | 0.672 |  | -22.4 | 16.2 |  | 112.9 | 100.8 |  | 86.3
7 | Laplacian |  | 1.804 |  | -18.6 | 9.3 |  | -155.5 | 98.8 |  | 82.7
8 | Laplacian |  | 1.823 |  | -20.8 | 9.3 |  | -155.5 | 98.8 |  | 82.7
9 | Laplacian |  | 1.851 |  | -22.6 | 9.3 |  | -155.5 | 98.8 |  | 82.7
10 | Laplacian |  | 2.497 |  | -22.3 | 19 |  | -143.3 | 100.8 |  | 82.9
11 | Laplacian |  | 3.509 |  | -25.6 | 32.7 |  | -94.7 | 96.4 |  | 88
12 | Laplacian |  | 5.152 |  | -20.2 | 0.5 |  | 147 | 98.9 |  | 81
13 | Laplacian |  | 11.342 |  | -29.8 | 55.9 |  | -36.2 | 95.6 |  | 88.6
15 | Laplacian |  | 19.514 |  | -29.2 | 57.6 |  | -26 | 104.6 |  | 78.3
 |  | Per-Cluster Parameters |  |  |  |  |  |  |  |  | 
 |  | Parameter |  | ASD | ASA | ZSD | ZSA |  |  | XPR | 
 |  | Unit |  | º | º | º | º |  |  | dB | 
 |  | Value |  | 5 | 11 | 3 | 7 |  |  | 8 | 

## Slide 7: TDL-E
Tap | Delay | Power | Fading distribution
# | s | dB | 
1 | 0 | 0 | Rice, K = 22 dB
2 | 0.485 | -15.8 | Rayleigh
3 | 0.514 | -18.1 | Rayleigh
4 | 0.532 | -19.8 | Rayleigh
5 | 0.514 | -22.9 | Rayleigh
6 | 0.672 | -22.4 | Rayleigh
7 | 1.804 | -18.6 | Rayleigh
8 | 1.823 | -20.8 | Rayleigh
9 | 1.851 | -22.6 | Rayleigh
10 | 2.497 | -22.3 | Rayleigh
11 | 3.509 | -25.6 | Rayleigh
12 | 5.152 | -20.2 | Rayleigh
13 | 11.342 | -29.8 | Rayleigh
14 | 19.514 | -29.2 | Rayleigh