## Slide 1: WF on UL RS for PUSCH
ZTE, …
R1-163544
3GPP TSG RAN WG1-#84b
April 15th - 19th, 2016, Busan, Korea
Agenda item 7.3.10.2

## Slide 2: Proposals for UL DMRS on slot-based TTI
  At least for slot-based TTI in low speed, legacy DMRS in one slot is reused to demodulate sPUSCH
    Further consider insertion of DMRS for higher speed

## Slide 3: Proposals for UL DMRS on 3/4symbols TTI
  For TTI with 3/4 symbols, DM-RS symbol in the 3rd symbol of a slot is shared by 2 short-TTIs within the slot to demodulate sPUSCH
  Following alternatives are considered for multiplexing DM-RSs of sPDSCHs from different short-TTIs:
  Using different CSs for UEs in different s-TTIs
  FDM between UEs in different s-TTIs
  DMRS of each s-TTI is generated according to a predefined frequency bandwidth granularity