## Slide 1
3GPP TSG RAN WG1 Meeting #84bis R1-163546
Busan, Korea, 11th - 15th April 2016
Agenda item: 7.3.3.1.2
WF on overhead reduction for Class B FD-MIMO with K = 1
Intel, Nokia, ASB

## Slide 2: Background
Beamformed CSI-RS resource for Class B FD-MIMO with K = 1 reuses the design from Rel-10 CSI-RS resource, where Rel-10 CSI-RS assumes non precoded CSI-RS
The design assumptions of Rel-10 non precoded CSI-RS are not valid for beamformed CSI-RS of Class B FD-MIMO with K = 1
  Due to beamforming for CSI-RS resource of Class B FD-MIMO with K = 1 the channel statistics in the frequency domain on CSI-RS antenna ports are substantially different from channel statistics of the channel on the non precoded CSI-RS antenna ports without beamforming
  The density of CSI-RS signals per PRB per antenna port for Class B FD-MIMO with K = 1 can be reduced comparing to density of non precoded CSI-RS

## Slide 3: Example of the channel transfer function on CSI-RS antenna port with and without beamforming

## Slide 4: Proposal
In Rel-14 antenna ports of NZP CSI-RS resource for Class B FD-MIMO with K = 1 can be transmitted every L-th PRB (L > 1)
  Details are FFS
  Other approaches for NZP CSI-RS overhead reduction are not precluded