## Slide 1: Way forward on the PSD Issue with RB-level Multi-cluster Transmission For: Decision AI: 7.3.1.1
Intel, Broadcom,…
3GPP TSG-RAN WG1 #84-bis R1-163572
Busan, Korea, Apr 11-15, 2016

## Slide 2: Background
In RAN1-84, the following agreement was made:
Agreement:
For eLAA, flexible timing between UL grant and UL transmission is supported
At least RB-level multi-cluster transmission (>2) is supported for eLAA PUSCH
  FFS: Detailed design
  FFS: Support of legacy resource allocation for PUSCH
On the other hand, PSD limit by ETSI and FCC are as follows:
EU: 10 dBm/1 MHz (5.15~5.35 GHz), 17 dBm/1 MHz (5.47~5.725 GHz)
FCC: 11 dBm/1 MHz (UNII-1,2A,2C), 30 dBm/ 500 kHz (UNII-3)

## Slide 3: Background
As an example, consider 10 dBm/1 MHz PSD limit with 23 dBm total transmit power limit.
With RB-level multi-cluster transmission, concentrating 10 dBm on one RB (180 kHz) is often considered:
When multiple UEs are multiplexed, they may transmit at their maximum transmit power:
The aggregate transmit power level can be much higher than when a single UE is scheduled:

## Slide 4: Background
To begin with, the goal of PSD limit is to maintain the spectrum flatness, since it is an unlicensed spectrum. If power concentration on arbitrarily narrow band is allowed, e.g., an extreme case of loading 10 dBm on single-tone, the spectrum flatness will be broken.
Furthermore, this can cause coexistence issues:
The total emission power can be 7 dB higher than neighboring LAA network serving single UE or neighboring Wi-Fi network.
When multiple UEs transmit at their maximum power at the same time, large surrounding area will be blocked.

## Slide 5: Proposal
RAN1 to consider the following candidate options:
  PSD limit is applied per any bandwidth.
  Multi-cluster transmission with each cluster consists of more than 6 consecutive RBs. (>1 MHz).
In parallel, RAN1 to send LS to ETSI BRAN and FCC, if a transmission narrower than ‘resolution’ bandwidth while not maintaining the spectrum flatness is allowed.