## Slide 1: WF on PUSCH transmissions in eLAA
Huawei, Hisilicon,…
3GPP TSG RAN WG1 #84bis R1-163584
Busan, Korea
11th – 15th April 2016
Agenda item: 7.3.1.1
Document for decision

## Slide 2: Proposal
Confirm the working assumption
The minimum latency is 4ms between the subframe carrying the UL grant and subframe(s) of the corresponding PUSCH(s)

## Slide 3: Proposal
For eLAA, the UL resource is divided into 10/5 interlaces and each interlace contains 10 evenly located RBs for 20MHz/10MHz bandwidth
  Design of resource allocation indication should balance the signaling overhead and allocation flexibility

## Slide 4: Proposals
For the UL DMRS for eLAA,
  Reuse the legacy UL DMRS generation sequence
  The symbol position of the UL DMRS of eLAA is the same as the UL DMRS position in LTE PUSCH subframe
  The frequency position of the UL DMRS is the same as the PUSCH REs