## Slide 1: WF on starting subframes of NB-PDCCH
Huawei, HiSilicon, …
R1-163587
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11-15 April, 2016
Agenda item 7.2.1.1.1

## Slide 2: Background
In eMTC, the start of a MPDCCH search space is defined as follows:
  For MPDCCH UE-specific search space, and Type0-MPDCCH common search space, the starting subframes are given by ,
where T=Rmax*G, G is from {1, 1.5, 2, 2.5, 4, 5, 8, 10} for FDD, and {1, 2, 4, 5, 8, 10, 20, reserved} for TDD and the index of one element is given by the higher layer parameter nPDCCH-startSF-UESS.

## Slide 3: Observations
The principle in eMTC can be reused for NB-IoT to define the start of NB-PDCCH search space. However,
  Some of the value(s) in the set G may not be appropriate for NB-IoT. For example, it was agreed that the start of an NB-PDCCH search space is >=4ms after the end of the last NB-PDCCH search space, i.e., Rmax(G-1)>=4ms, excluding the value “1” from G.
  For small values of Rmax, sufficiently large value(s) in G should be provided to ensure low power consumption for good coverage UEs. If the set of G in eMTC is reused, the resulting largest period (e.g. 10 for Rmax=1) are felt too small.
  For large values of Rmax, a sufficient number of small values in G should be provided such that the period is not too large (i.e. <= 2560ms as in eMTC). As can be seen in the following table, if the set of G in eMTC is fully reused, no valid period is available for Rmax=2048.

## Slide 4: Observations
Rmax | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
G |  |  |  |  |  |  |  |  |  |  |  | 
1 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
1.5 | 1.5 | 3 | 6 | 12 | 24 | 48 | 96 | 192 | 384 | 768 | 1536 | 3072
2 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
2.5 | 2.5 | 5 | 10 | 20 | 40 | 80 | 160 | 320 | 640 | 1280 | 2560 | 5120
4 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
5 | 5 | 10 | 20 | 40 | 80 | 160 | 320 | 640 | 1280 | 2560 | 5120 | 10240
8 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384
10 | 10 | 20 | 40 | 80 | 160 | 320 | 640 | 1280 | 2560 | 5120 | 10240 | 20480
List of periods if the set of G in eMTC is reused.

## Slide 5: Proposals
For NB-PDCCH search space for UE-SS and CSS for RAR/Msg3 re-transmission/Msg4, the starting subframes are given by,
where T=Rmax*GRmax.
  For each Rmax, the corresponding set of values of parameter GRmax is
where [g0, g1, g2, …, g11] = [1.25, 2, 3, 4, 6, 8, 12, 16, 24, 32, 64, 128]
And then one element in the set is chosen as GRmax by 3-bit higher layer signaling.

## Slide 6: Observations
List of periods if the proposed set of G is used.
Rmax | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048
GRmax |  |  |  |  |  |  |  |  |  |  |  | 
g0=1.25 | 1.25 | 2.5 | 5 | 10 | 20 | 40 | 80 | 160 | 320 | 640 | 1280 | 2560
g1=2 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
g2=3 | 3 | 6 | 12 | 24 | 48 | 96 | 192 | 384 | 768 | 1536 | 3072 | 6144
g3=4 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
g4=6 | 6 | 12 | 24 | 48 | 96 | 192 | 384 | 768 | 1536 | 3072 | 6144 | …
g5=8 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | … | …
g6=12 | 12 | 24 | 48 | 96 | 192 | 384 | 768 | 1536 | 3072 | 6144 | … | …
g7=16 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | … | … | …
g8=24 | 24 | 48 | 96 | 192 | 384 | 768 | 1536 | 3072 | 6144 | … | … | …
g9=32 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | … | … | … | …
g10=64 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | … | … | … | …
g11=128 | 128 | 256 | 512 | 1024 | 2048 | … | … | … | … | … | … | …